Maine Greenhouse Gas Action Plan Development Process

Buildings, Facilities & Manufacturing Processes Greenhouse Gas Reduction Options

Center for Clean Air Policy

January 16th, 2004

Contents												Page

- Overview………………………………………………………………………..2

- Criteria for Assessing and Measuring GHG Measures…………………………3

- Potential B,F&M GHG Reduction Opportunities –Edited 12-17-03…………...4

- Preliminary GHG Savings & Cost Estimates for Priority Measures…………..10

- BFM Assumptions……………………………………………………………...11

1.  Overview

Under the direction of DEP, the Center for Clean Air Policy (CCAP) developed a set of primary and secondary criteria for assessing and prioritizing GHG measures in advance of the second Stakeholder meeting on December 17th, 2003.  The two primary criteria are the potential GHG reduction by 2020, and the cost effectiveness of these reductions.  This list of criteria can be found in Section 2 of this document.

CCAP also developed an extensive list of Greenhouse Gas Reduction options for Maine, in advance of the December 17th meeting.  Options that were popular choices in other states, or potentially high Maine GHG reduction options, or both, were denoted with a * by CCAP.  At the 12/17 meeting, the Stakeholder Advisory Group reviewed and commented on the list of options.  This Buildings, Facilities, and Manufacturing list of options can be found in Section 3 of this document.

CCAP then took this revised list of priority options, and developed preliminary GHG savings and cost estimates (see Section 4) for the priority measures identified from the 12/17 meeting.  To accompany the preliminary GHG savings and cost estimates, CCAP created a BFM assumptions document to identify underlying data sources and assumptions, as well areas where additional information is needed (Section 5).

2. Proposed Criteria for Assessing and Prioritizing GHG Measures

| PRIMARY CRITERIA | Indicators that would be assessed by CCAP to the extent possible using the best available data for each option. |
| --- | --- |
| GHG Impact | Total annual GHG’s reduced in relevant target years in carbon equivalents. This is typically expressed as an average annual level of projected MMTCE reduction in a given year beyond baseline emissions. GHG impacts must be quantified in order to aggregate measures toward a numerical target. |
| Cost-Effectiveness | Direct net cost divided by the GHG impact (expressed in dollars per metric ton of carbon equivalent) and is typically expressed in a given year as an average annual value over the life of the action. Costs may be expressed as a range. |
| SECONDARY CRITERIA | Indicators that would be assessed by CCAP, the Working Groups, or both when relevant for a particular option using best available data. These impacts may not be readily quantifiable. |
| Ancillary Environmental Impacts | Environmental impacts other than GHG emissions reductions, including public health and ecosystem impacts from changes in air quality or other environmental indicators. These impacts may not be readily quantifiable. |
| Ancillary Economic Impacts | Economic impacts other than direct costs or benefits of GHG reduction actions (e.g. economic development, cost savings for other actions). These impacts may not be readily quantifiable. |
| Equity Effects | Measure disproportionately affects a population, sector or a region of the state or affects the state’s competitive position relative to other states. These impacts may not be readily quantifiable. |
| Public and Political Support/Concern | Expected support and or concern from the general public and from policymakers. These impacts may not be readily quantifiable. |
| Feasibility | Ease of implementation and administration by implementing parties. These impacts may not be readily quantifiable. |
| Compatibility | Measure reinforces or enhances the effectiveness of other policy programs, or is required for other measures to work. These impacts may not be readily quantifiable. |
| Transferability to Other States/Nationally | Ease of duplication of measure in other states and or national and international policies. These impacts may not be readily quantifiable. |

- Potential B,F&M GHG Reduction Opportunities –Edited 12-17-03

The following notation was used in the table below:

- *Options that were popular choices in other states, potentially high Maine GHG reduction options, or both (originally denoted by CCAP, reviewed by Stakeholders

- *?  For *’d options to which at least one member of the Stakeholder Advisory Group expressed uncertainty about it being important in Maine

- *! For options not previously marked with a *, which at least one member of the Stakeholder Advisory Group thought should be a priority

- Some additional comments from stakeholders are highlighted in the list

| Residential Sector GHG Reduction Opportunities |
| --- |
| 1 | Improve Energy Efficiency (EE) of Appliances |
| 1.1 | *Energy Efficiency Appliance Standards - For appliances not covered under federal standards, the state can set minimum levels of efficiency for specific appliances. |
| 1.2 | Tax Incentives for EE Appliances |
| 1.3 | Discounts/Rebates on Energy Star Products |
| 1.4 | Contractor Education: Proper sizing of HVAC – Proper sizing of air ducts and other components of heating, ventilation and air conditioning systems can significantly reduce the size and energy requirements of furnaces and air conditioning units. |
| 1.5 | Consumer Education: Selection, Alternate appliance choices – Educate consumers about the lifetime savings achieved over appliance lifetime by appliances that consume less energy. |
| 1.6 | Bulk Purchasing Program - Bulk procurement can reduce the cost of energy efficient appliances or renewable technologies. |
| 1.7 | Promote Appliance Recycling |
| 1.7.a | Appliance recycling pick-up program – Program to collect and recycle old residential appliances, rather than send them to junkyards/landfills. |
| 1.7.b | Reduce secondary market for used appliances – Create incentives for residential customers to discard old appliances when new ones are purchased, rather than selling the old appliance or running both the new and old appliance (e.g. air conditioners or refrigerators). Other states have offered a “bounty” rebate to residents who buy a new window AC unit and turn in the old unit to the state for disposal. |
| 2 | Incentives to Technology Providers |
| 2.1 | R&D |
| 2.2 | Incentives to manufacturers (regional) –Cross cutting for all GHG sectors |
| 3 | Improve EE and Sustainable Design of Buildings |
| 3.1 | *Improved Building Codes (revisit every 3 years) - Require buildings to meet the most recent Energy Code efficiency/performance standards established by the International Code Council. (Avoid conflict with Rehab code) |
| 3.2 | *!Training (builders, code officials, architects etc.) and Enforcement of Building Codes |
| 3.3 | EPA Energy Star Homes - This program provides rebates for the purchase of newly constructed homes meeting higher efficiency standards established by the U.S. EPA and DOE Energy Star Program. |
| 3.4 | *!Voluntary Green Building Design Standards – Create voluntary high efficiency and sustainable building standards (recycled material, low VOC content, low embodied energy construction materials, etc.) that builders can follow. Buildings meeting the standards can have a “seal of approval” or other type of recognition (e.g., LEED). |
| 3.5 | Mandatory "Green" Standards for New Construction/ Renovations |
| 3.6 | *Energy Efficiency Mortgages - Energy Efficient Mortgages allow purchasers to borrow a larger mortgage when purchasing an Energy Star home. Energy Improvement Mortgages allow owners to borrow money for energy efficiency improvements on their homes, or to upgrade the energy efficiency of a home before purchasing. |
| 3.7 | Financial incentives for contractors, builders, homeowners |
| 3.8 | Increased marketing of existing programs |
| 3.9 | White Roofs and Rooftop Gardens – Reflect sunlight and shade roofs to reduce air conditioning energy requirements. |
| 3.10 | Landscaping – Well-planned landscaping with trees for shade and evergreens/hedges to block wind reduce a building’s heating and cooling requirements. |
| 3.11 | *Education to homeowners – Educate homeowners energy efficiency and sustainable design retrofits, renovations and new construction options. |
| 4 | Improve Energy Management |
| 4.1 | Energy Audits – Assess a home’s energy use, and areas where energy is being wasted. |
| 4.1.a | Weatherization |
| 4.1.b | Blower door testing |
| 4.2 | Training of Building Operators |
| 4.3 | Efficient Use of Oil and Gas |
| 4.3.a | Improve building envelope – windows, insulation, etc. |
| 4.3.b | *Heating |
| 4.3.c | DHW |
| 4.3.d | Cooking |
| 4.3.e | Pumping well water |
| 4.3.f | Fuel Switching to less carbon-intensive fuels |
| 4.4 | Efficient Use of Electricity |
| 4.5 | *Educate residents/ public/ children |
| 4.5.a | Marketing Programs |
| 4.5.b | Introduce in School Curriculum |
| 4.6 | Advanced metering – Provides real or near real-time electricity consumption data. Combined with time-of-use rates, creates incentive for residential electricity load management and conservation. |
| 4.7 | Load Management – With advanced meters and time-of-use rates in place, residential electricity customers can manage their energy use to reduce consumption during peak daytime rates, thereby saving money. |
| 4.8 | Time-of-Use (TOU) Rates – Time-of-use rates for electricity, a market mechanism charging customers more during daytime peak periods and less during off-peak periods. Provides incentive for residential customers to save money by shifting some energy consuming tasks (such as laundry) to off-peak periods. |
|  | See also "Comprehensive Programs" |
| Commercial Sector GHG Reduction Opportunities |
| 1 | Improve Energy Efficiency (EE) of Equipment and Appliances |
| 1.1 | *EE Equipment and Appliance Standards - For appliances not covered under federal standards, the state can set minimum levels of efficiency for specific appliances. |
| 1.2 | Tax Incentives for EE Equipment and Appliances |
| 1.3 | Discounts on Energy Star Products |
| 1.4 | Bulk Purchasing Program - Bulk procurement can reduce the cost of energy efficient appliances or renewable technologies. |
| 2 | Energy Efficient Buildings |
| 2.1 | *Improved Building Codes - Require buildings to meet the most recent Energy Code efficiency/performance standards established by the International Code Council. |
| 2.2 | Training (Builders, Code Officials, Architects etc.) and Enforcement of Building Codes |
| 2.3 | Voluntary Green Building Design Standards |
| 2.4 | *"Green" Standards for New Construction/ Renovations |
| 2.4.a | Mandatory standards for state buildings - Construction and renovations receiving any state funding should meet higher energy efficiency/performance standards. |
| 2.4.b | Mandatory standards for schools - Construction and renovations receiving any state funding should meet higher energy efficiency/performance standards. |
| 2.5 | *Incentive payment for green buildings - Provide incentives for privately financed new construction and renovation to meet higher energy efficiency performance standards than standard construction. |
| 2.6 | White Roofs and Rooftop Gardens – Designed to reduce solar heat gain and thereby reduce air conditioning electricity needs. |
| 2.7 | *State-wide EE Goals and Reporting for Government Buildings - A program to encourage measurement and tracking of energy consumption, strategic planning and benchmarking against other buildings. |
| 3 | Improve Energy Management |
| 3.1 | Energy Audits |
| 3.2 | Building Recommisioning |
| 3.3 | Training of Building Operators - Training building operators in how to maximize the efficiency of their buildings will decrease energy use if operators apply what they learned. |
| 3.4 | Efficient Use of Oil and Gas |
| 3.4.a | Building Shell – Windows, insulation, etc. |
| 3.4.b | Heating |
| 3.4.c | DHW |
| 3.5 | Efficient Use of Electricity |
| 3.5.a | Lighting |
| 3.5.b | A/C |
| 3.5.c | Ventilation |
| 3.5.d | Pumps/motors |
| 3.6 | *Shared Savings Program for Government Agencies - Allows a state agency to keep a portion of the energy savings realized when the agency makes energy efficiency improvements to a building. |
| 3.7 | Fuel Switching to less carbon-intensive fuels – such as natural gas, biodiesel, etc. |
| 3.8 | *Load Management |
| 3.9 | *!Green campus initiative –already begun. |
| 4 | Promote Recycling |
|  | See also "Comprehensive Programs" |
| Industrial Sector GHG Reduction Opportunities |
| 1 | Industrial Energy Efficiency (EE), Management, and Conservation |
| 1.1 | Efficient Use of Oil and Gas |
| 1.1.a | Boilers |
| 1.1.b | Upgrade to steam system |
| 1.1.c | Process-specific equipment |
| 1.1.d | Building Envelope – Windows, insulation, etc. |
| 1.2 | Efficient Use of Electricity |
| 1.2.a | Pumps |
| 1.2.b | Motors |
| 1.2.c | Lighting |
| 1.2.d | Cooling |
| 1.3 | Optimization of Compressed air systems |
| 1.4 | EE process improvements |
| 1.5 | Shut-it off program (curtailment) – Financial incentive for industrial electricity customers to cut demand during peak/emergency demand periods for the local utility. |
| 1.6 | Energy Management Training |
| 1.7 | R&D of new technologies |
| 1.8 | *Financial incentives - Offer incentive rebates for energy efficiency improvements. |
| 1.9 | Education |
| 2 | Reduction in Process Gases |
| 2.1 | *Participate in Voluntary Industry-Government Partnerships |
| 2.2 | *Leak Reduction Programs |
| 2.3 | Process Changes/ Optimization |
| 2.4 | Capture, Recovery and Recycling of Process Gases |
| 2.5 | New Equipment |
| 2.6 | *!Substitution of High GWP Gases – Substitute high global warming potential (GWP) gases with appropriate substitutes depending on application (e.g., CO2, ammonia). |
| 3 | Supply Side Measures |
| 3.1 | *Encourage Combined Heat and Power – Combined heat and power is a high efficiency method of distributed generation that utilizes both the steam and electricity produced from the electricity generating process, rather than just the electricity. Efficiency can be 2-3 times that of systems not utilizing the heat produced. |
| 4 | Other programs |
| 4.1 | *!Industrial ecology/ by-product synergy – Programs to link the by-products from one industry with use as the feedstock for other industries. |
| 4.2 | *!Negotiated Agreements - To promote GHG reductions in particular sectors, a state government may enter into direct voluntary or negotiated agreements with industries or industrial sectors. Legislation requires (need to develop metrics) |
| 4.3 | Cap and Trade |
|  | See also “Comprehensive Programs” |
| Comprehensive Programs for Residential, Commercial and Industrial Sectors GHG Reduction |
| 1.1 | Mandatory Reporting of Fuel Use, GHG Emissions |
| 1.2 | State-wide Energy Efficiency/GHG Emission Reduction Goals |
| 1.3 | *Government Agency Requirements and Goals |
| 1.4 | *Public Benefit Funds – Funds created by a surcharge on electricity, natural gas or oil sales that are used to fund demand side energy efficiency and conservation programs. |
| 1.5 | Negotiated Agreements |
| 1.6 | Environmentally Friendly Procurement |
| 1.7 | Small-source aggregation |
| 1.8 | Supply-Side Measures |
| 1.8.a | Net-metering - Allows the electric meters of customers with generating facilities to turn backwards when the generators are producing energy in excess of the customers' demand, enables customers to use their own generation to offset their consumption over a billing period. |
| 1.8.b | Encourage Green Power Purchases |
| 1.8.c | Incentives for Renewable Energy Applications |

4.  Preliminary GHG Savings & Cost Estimates for Priority Measures

5.BFM Assumptions

Appliances

BFM 1.1  Energy Efficiency Appliance Standards (R/C)	12

Residential

BFM 2.1  Improved Building Energy Codes (R/C)	13

BFM 2.2  Training and Enforcement of Building Codes (R/C)	15

BFM 2.3 Voluntary Green Building Design Standards	16

BFM 2.4 Energy Efficiency Mortgages	17

BFM 2.5  Education to homeowners	18

BFM 2.6  Efficient Use of Oil and Gas:  Home Heating	19

Commercial

BFM 3.1 Green standards for New construction/Renovations	20

BFM 3.2  Incentive Payment for Green Buildings	21

BFM 3.3 State-wide EE Goals and Reporting for Government Buildings	22

BFM 3.4 Shared Savings Program for Government Agencies	23

BFM 3.5 Load Management	25

BFM 3.6 Green Campus Initiatives	26

Industrial

BFM 4.1 Financial Incentives for Industrial EE	27

BFM 4.2 Participate in Voluntary Industry-Government Partnerships	28

BFM 4.2 Leak Reduction Programs	29

BFM 4.3  Substitution of High GWP Gases	30

Encourage Combined Heat and Power	31

BFM 4.4 Industrial ecology/by-product synergy	32

BFM 4.5 Negotiated Agreements	33

Comprehensive

BFM 5.1  Government Agency Requirement and Goals	34

BFM 5.2  Public Benefit Fund	35

BFM 5.3  Educate residents/public/children	36

| Measure: | BFM 1.1 Energy Efficiency Appliance Standards (R/C) |
| --- | --- |

# Sector:			Residential, Commercial

Policy Description:	For appliances not covered under federal standards, the state can set minimum levels of efficiency for specific appliances.

# BAU Policy/Program:	Legislation proposed, not passed.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Set minimum efficiency standards for the following products:

| Product | Unit Sales in ME * | Savings in 2010 (GWh or BBtu) | Savings in 2020 (GWH or BBtu) | Unit Savings (kWh or therm) | Lifetime | Incremental Cost ($) |
| --- | --- | --- | --- | --- | --- | --- |
| Dry type transformers | 61,758 | 6.9 | 19.3 | 16.6 | 30 | 9 |
| Commercial refrigerators & freezers | 569 | 1.2 | 2 | 1542 | 9 | 115 |
| Exit signs | 14,624 | 3.7 | 10.3 | 223 | 2.5 | 30 |
| Traffic signals | 808 | 1.7 | 3.1 | 431 | 15 | 125 |
| Torchiere lamps | 49,267 | 66.9 | 121.7 | 288 | 10 | 40 |
| Set-Top boxes |  | 96.7 | 96.7 |  |  |  |
| Unit heaters (therm savings) | 197 | 68.3 | 179.7 | 268 | 18 | 425 |
| Commercial Clothes Washers | 2,031 | 1.2 | 1.8 | 197 | 8 | 200 |

Source: ENE, Communication with M Stoddard; NEEP, 2003

*Unit sales estimated based on energy savings in 2010, update as data becomes available.

# All of these appliances can be regulated by the state, and do not require a federal waiver.

| Measure: | BFM 2.1 Improved Building Energy Codes (R/C) |
| --- | --- |

# Sector:	Residential, Commercial

Policy Description:	Require buildings to meet the most recent energy code efficiency/performance standards established by the International Code Council.  Revisit every 3 years.

BAU Policy/Program:	Residential: State-developed code, less stringent than 1992 MEC, mandatory statewide

Commercial: ASHRAE/IESNA 90.1-2001, mandatory statewide; can COM check -EZ to show compliance.  (Most up to date)

Maine has held four meetings of the Building Code Working Group starting in March 2003. The purpose of this group is to 1.) Survey stakeholders and determine where they stand on the issues 2.) Determine which code, NFPA or ICC, to adopt 3.) Make recommendations on how the chosen code is going to be implemented and enforced. (Source: www.bcap-energy.org)

DPUC Working Group also.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

- Residential building codes are updated every 3 years and adopted by ME 18 months thereafter.

# Update commercial building codes 18 months after they are adopted (assume 2008).  Continue to update 18 months after new codes are developed thereafter.

# Each building code revision achieves the same level of savings.

# Estimates only include residential building savings; commercial building savings are not available at this time.

| Data Need | Assumption | Source |
| --- | --- | --- |
| Annual Residential Savings |  |  |
| Oil savings per home | 18.4% | Xenergy, 2001. "Impact Analysis of the Massachusetts 1998 Energy Code Revisions" |
| Natural gas savings per home | 13.7% | Xenergy, 2001 |
| Electricity savings per home | 1.1% | Xenergy, 2001 |
| New residential buildings built each year | 5,000 | CT data scaled to ME based on US census data |
| Number of residential buildings that comply with new codes | 60% | Estimated |
| Increased cost for new residential codes building codes | NA |  |
| Annual Commercial Savings |  |  |
| Oil savings | NA |  |
| Natural gas savings | NA |  |
| Electricity savings | NA |  |
| New commercial buildings built each year | 2,184 | CT data scaled to ME |
| Number of commercial buildings that comply with new codes | 60% | Estimated |
| Increased cost for new commercial building codes | NA |  |

# NA:  Data not available at this time

Potential Barriers/Issues:  Avoid conflict with Rehab code

| Measure: | BFM 2.2 Training and Enforcement of Building Codes (R/C) |
| --- | --- |

# Sector:	Residential, Commercial

Policy Description:	Building codes are not effective unless implemented.  Train builders, code officials, architects, etc. on building codes

BAU Policy/Program:	Maine DPUC has joined with NEEP’s “Northeast Regional Building Energy Codes Project” to enforce building codes.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

For preliminary analysis, following assumptions were made:

# Improve number of buildings that comply with building codes by 10%

# Energy savings based on assumptions of improved building code (see previous measure)

# Cost data not available at this time.

# Savings associated with commercial building codes are not available at this time; estimate includes only residential building code upgrades.

| Measure: | BFM 2.3 Voluntary Green Building Design Standards |
| --- | --- |

# Sector:	Residential

Policy Description:	Create voluntary high efficiency and sustainable building standards that builders can follow (e.g., Energy Star).

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Number of new homes built in ME | 5,006 | CT data scaled based on US Census data |
| Number of new homes meeting higher standard | 10% per year | Estimated |
| Savings between Energy Star and standard construction | 30% | EPA |
| Incremental Cost between Energy Star and standard construction | $2150/home | EPA |

| Measure: | BFM 2.4 Energy Efficiency Mortgages |
| --- | --- |

# Sector:	Residential

Policy Description:	Energy Efficient Mortgages (EEMS) allow the buyers of EE homes to qualify for more debt because of their lowered monthly utility costs. This stretch allows more buyers to afford the higher quality, EE homes. This program has worked best when a home energy rating system is available to document the relative efficiency of a home.

Energy Improvement Mortgages (EIMs) - This type of EE mortgage finances cost-effective improvements recommended in an energy rating through the mortgage at the time of sale or refinancing. The funds for the improvements are placed into an escrow by the lending institution. Once the improvements are made, a post-improvement home energy rating is performed to confirm the improvements were installed. The lending institution then releases the escrow funds to pay for materials and contracted labor. The total expended is rolled into the mortgage loan.

BAU Policy/Program:	Fannie Mae and Freddie Mac are piloting effort in Alaska, Arkansas, Colorado, Iowa, Louisiana, Mississippi, Vermont, and Wisconsin.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Average annual energy savings per home | 6.4 MMBTU | Energy Rated Homes of Vermont |
| Resale activity each year in ME | 38,700 | National Association of Realtors |
| Number of home buyers participating in Mortgage Program | 1% | Estimate |

| Measure: | BFM 2.5 Education to homeowners |
| --- | --- |

# Sector:	Residential

Policy Description:	Educate homeowners on EE and sustainable design retrofits, renovations and new construction options (e.g., provide EE education materials at time of resale or refinancing).

BAU Policy/Program:	Education programs under Efficiency Maine; Programs by DEP

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# What type of program is envisioned?

# When/Where/How would homeowners be targeted?

# During building inspection at time of resale

# Mandatory efficiency ratings on furnaces/boilers/other equipment

# Through electricity billing

| Measure: | BFM 2.6 Efficient Use of Oil and Gas: Home Heating |
| --- | --- |

# Sector:	Residential

Policy Description:	Provide incentives for EE retrofits or upgrades for home heating equipment

BAU Policy/Program:	LIHEAP, WAP, REACH Central Heating Improvement (CHIP) Programs for low-income residents. (Energy Advisors, LLC, 2003)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Sources |
| --- | --- | --- |
| Oil Furnaces/Boilers |  |  |
| Number of operating at or below 60% efficiency | 15% | Estimated |
| Savings associated with replacing 60% efficient furnace with Energy Star oil Furnace (90%) | 40 MMBTU/furnace | EPA |
| Incremental cost of Energy Star Oil Furnace | $2700/furnace | Consumer Energy Council of America, 2001 |
| Market penetration | 2% | Estimated |

80% of the heating in the residential sector is provided by oil; only measure to replace oil furnaces investigated at present.

| Measure: | BFM 3.1 Green standards for New construction/Renovations |
| --- | --- |

## Sector:			Commercial

Policy Description:	New construction as well as major renovations of all building projects that receive some state funding (state facilities, local schools, etc.) should be required to meet LEED Silver.

BAU Policy/Program:	The State of Maine has recently passed two pieces of legislation regarding this issue:  1) The Development of optimal energy efficiency in state state-funded construction (requires buildings be designed and built to standards of energy efficiency that are always at least 30% higher than the minimum energy standard s required by current state energy codes), and 2) Construction of schools (amends rules on construction of new schools to require that all construction proposals must be based on the most energy and environmentally efficient designs suitable).

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Legislation exists for publicly funded buildings

- Assumed zero savings above business-as-usual

| Data Needs | Assumptions | Sources |
| --- | --- | --- |
| Number of state-funded buildings built each year |  |  |
| Energy savings per year | 30% | Steven Winters Associates |
| Incremental cost | $225.55/sq ft | NYSERDA |

| Measure: | BFM 3.2 Incentive Payment for Green Buildings |
| --- | --- |

## Sector:			Commercial

# Policy Description:	Encourage privately financed new construction and renovation to be high performance buildings by certifying to LEED standard.

# Provide tax credits and other financial incentives for green buildings, similar to those offered in NY and MA.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Number of commercial buildings built each year | 2,184 | CT data scaled to ME |
| Market penetration | 2% | Estimate |
| Energy Savings for LEED Silver compared with 1989 Building Code | 25% | Steven Winters Associates |
| Cost Estimate | 2-7% increase of initial costs | US Green Building Council |

| Measure: | BFM 3.3 State-wide EE Goals and Reporting for Government Buildings |
| --- | --- |

# Sector:	Commercial/Government Agency Buildings

Policy Description:	A program to encourage measurement and tracking of energy consumption, strategic planning, and benchmarking against other buildings.

BAU Policy/Program:	 25% energy reduction goal by 2010 (relative to 1998 baseline) added to Energy Conservation Building Act for Public Buildings. This legislation established a pilot program to seek to achieve that level of energy savings in ten facilities of over 40,000 square feet. Under the pilot program, energy savings are to be achieved through performance contracts with energy service companies.

LD845 Climate Change:  This bill requires new sources of greenhouse gases to be reported to the Department of Environmental Protection.  It also requires the department to create an inventory of greenhouse gas emissions associated with state-owned facilities and state-funded programs and to create a plan for reducing those emissions.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

- Savings will show up in shared savings program.  Benchmarking will help to identify which buildings to pursue first.

| Measure: | BFM 3.4 Shared Savings Program for Government Agencies |
| --- | --- |

# Sector:	Commercial/Government Agency Buildings

Policy Description:	Incentive program for state agencies achieving savings through energy conservation, with portion of savings retained by agency for future energy costs/activities.

BAU Policy/Program:	Under a law passed in 1991, the Bureau of Public Improvements (predecessor to the Bureau of General Services) was charged with developing a program “in which an eligible department or agency of the State may retain a portion of any first-year energy cost savings demonstrably attributable to energy efficiency improvements undertaken by that department or agency.”105 The Bureau was required to submit the proposed program to the legislative Committee on State and Local Government by January 1, 1992. It does not appear that this program was ever implemented. (Energy Advisors, LLC, 2003)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| State Agency Fuel Consumption |  |  |
| Electricity | 127,384 MWh | Energy Advisors, LLC |
| Natural Gas | 90,025 | Estimated using government to commercial sector electricity share |
| Oil | 643,062 MMBTU | Estimated using government to commercial sector electricity share |
| Government building share of commercial sector electricity consumption | 3% | Energy Advisors, LLC |
| Reduction in state energy use by 2010 | 20% | Estimated |
| Reduction in state energy use by 2020 | 50% | Estimated |

| Measure: | BFM 3.5 Load Management |
| --- | --- |

# Sector:	Commercial

# Policy Description:	Overcome existing regulatory barriers to increase the market diffusion of third party load management for non-intrusive commercial loads (e.g., dimming lights, planned cycling of refrigeration compressors)

## BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Market Size | 1250 MW | Scaled CT market size to ME based on share of commercial electricity consumption |
| Market Penetration per year | 5% | Estimated |
| Incremental Cost | NA |  |

NA: Data not available at this time

| Measure: | BFM 3.6 Green Campus Initiatives |
| --- | --- |

Sector:	Commercial

Policy Description:  	Promote a “Green Campus” Initiative with all Maine Colleges, Universities, Private/Secondary Schools with Campus to minimize environmental impact

# BAU Policy/Program:  	Currently underway

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Duration of Proposed Program | 5 years | Estimated |
| Market Size | 27 colleges and universities with 52,441 student enrollment | Department of Education |
| Average $/student for energy | $642.22/Student | DOE; based on public four year institution |
| % of Market enrolled in program each year | 20% | Estimated |
| Average electricity savings | 35% | DOE “Energy Smart Guide to Campus Cost Savings” |
| Average fossil fuel reductions | 25% | DOE “Energy Smart Guide to Campus Cost Savings” |

| Measure: | BFM 4.1 Financial Incentives for Industrial EE |
| --- | --- |

# Sector:	Industrial

Policy Description:	Offer financial incentive/rebates for EE improvements taken at ME industries

# BAU Policy/Program:	Efficiency Maine has established a new Commercial and Industrial Program for Maine businesses that provides a combination of services, including energy efficiency information and training, business practice assistance, and direct financial incentives in the form of grants. The components of the program are designed to encourage businesses to adopt energy efficient business practices, to include consideration of energy costs and energy efficiency in their business decisions, and to purchase and install energy efficient products.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Performance of Efficiency Maine’s C&I program | 10 kWh/$ | CT’s Energy Opportunities program; up to 30% cost share |
| Level of increased funding | $2 million | Estimate |

| Measure: | BFM 4.2 Participate in Voluntary Industry-Government Partnerships |
| --- | --- |

## Sector:			Commercial, Industrial

Policy Description:	Strongly promote voluntary programs and actions to the appropriate sectors. While some programs already exist at the national level, there may also be an opportunity to develop additional programs in Maine.

BAU Policy/Program:   	Several programs already exist at the national level:  EPA Climate Leaders, DOE Industries of the Future (Maine Industries of the Future currently includes pulp and paper, secondary wood, and metals industry), EPA Energy Star Benchmarking Program, DOE Rebuild America; Maine STEP-UP program

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# DOEs suggestions for expanding Maine participation in IOF:

# Include agriculture and plastics and potentially welding

# Additional publicity

# The Maine legislature might consider creating a mini state grant program that could provide funds to Maine businesses for feasibility studies to determine whether to adopt new energy-efficient technologies.

# Discuss energy and EE technologies as part of technology cluster project

# The Maine Smart Tracks for Exceptional Performers and Upward Performers, or STEP-UP, Program offers recognition and other incentives to businesses interested in implementing sustainable practices.

# Alan Auto (Portland), Bath Iron Works (Bath), Fairchild Semiconductor (South Portland), Interface Fabrics Group (Guilford), Moss, Inc. (Belfast), NorDx (Scarborough) and Poland Springs Bottling Company (Hollis). College of the Atlantic (Bar Harbor), CYRO Industries (Sanford), National Semiconductor of Maine (South Portland) and Naturally Potatoes (Mars Hill).

| Measure: | BFM 4.2 Leak Reduction Programs |
| --- | --- |

# Sector:	Industrial

Policy Description:	Reduce methane leaks from natural gas systems, reduce HFC leaks from refrigeration, motor vehicle air conditioning, etc.

BAU Policy/Program:   	Existing federal programs to reduce methane leaks from natural gas pipelines, SF6 from electricity substations

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Increased participation in EPA Natural Gas Star | NA |  |
| Increased participation in SF6 Electrical Utility | NA |  |
| ODS substitute emissions from refrigeration and A/C | 67% | US EPA based on national statistics |
| HFC emissions from stationary refrigeration | 40% | USEPA based on national statistics |
| Market penetration | 5% per year | Estimated |
| HFC leak reduction potential for stationary refrigerants | 5% | US EPA |

# NA: Data not available at this time

| Measure: | BFM 4.3 Substitution of High GWP Gases |
| --- | --- |

# Sector:	Industrial

Policy Description:	 Substituting other gases for high GWP gases is a viable option as long as environmental, health, safety, and performance requirements can be met.

BAU Policy/Program:   	None.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Alternative Refrigerants

# Ammonia. Ammonia, primarily used in water cooled chillers, has excellent thermodynamic properties and can be used in many types of systems. However, it must be used carefully, because it is toxic and slightly flammable.  Building and fire codes restrict the use of ammonia in the urban areas of the United States and many other countries. (EPA, 2001)

# Hydrocarbons. Hydrocarbons have thermodynamic properties that make them good refrigerants; however, their high flammability causes concern for safety. Hydrocarbon refrigerant use is generally restricted by U.S. safety codes, with the exception of industrial refrigeration(EPA, 2001).

# Carbon Dioxide. Carbon dioxide has been investigated for use primarily in mobile air-conditioning systems and refrigerated transport. (EPA, 2001)

# Alternative Solvent Fluids

# In electronics, metal, and some precision cleaning end uses, alternative organic solvents with lower GWPs are being manufactured and integrated into the industry. Some of these solvents, such as HFCs, HFEs, hydrocarbons, alcohols, volatile methyl siloxanes, brominated solvents, and non-ODS chlorinated solvents, can be used as alternatives to PFC/PFPEs, CFCs, and HCFCs.

# Non-HFC Blowing Agents

# Hydrocarbons (HC) Hydrocarbons such as propane and butane are alternatives to HFCs. HCs are inexpensive and have lower GWP impacts relative to HFCs. However, key technical issues associated with hydrocarbons are: flammability, VOCx, and performance.

# Liquid Carbon Dioxide (LCD).  Foams blown with CO2 might suffer from lower thermal conductivity, lower dimensional stability, and higher density versus HCFC blown foams. To overcome these limitations, CO2 can be blended with hydrocarbons or HFCs.

# Water-Blown (in situ) Carbon Dioxide (CO2/water).  During manufacturing, no ODP or high GWP gases are emitted, and there are limited  health and safety risks during processing. However, foams produced using CO2/water are subject to the same performance limitations discussed for LCD-blown foams

# Lower-GWP HFC Substitution.  Manufactures can reduce their emissions on a carbon basis by switching from a blowing agent with a high GWP to one with a lower GWP, but any associated energy penalties must also be considered.

| Measure: | Encourage Combined Heat and Power |
| --- | --- |

# Sector:	Industrial

Policy Description:	Combined heat and power (CHP) is the simultaneous production of electricity and heat using a single fuel. The heat produced from the electricity generating process is captured and utilized to produce high and low level steam. The steam can be used as a heat source for both industrial and domestic purposes and can be used in steam turbines to generate additional electricity (combined cycle power).

BAU Policy/Program:

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# To be covered by the Electricity Working Group

| Measure: | BFM 4.4 Industrial ecology/by-product synergy |
| --- | --- |

# Sector:	Industrial

Policy Description:	Programs to link the by-products from one industry with use as the feedstock for other industries.

BAU Policy/Program:   	None.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Measure: | BFM 4.5 Negotiated Agreements |
| --- | --- |

# Sector:	Industrial

Policy Description:	To promote GHG reductions in particular sectors, a state government may enter into direct voluntary or negotiated agreements with industries or industrial sectors. Negotiated agreements, for example, would result in agreed-upon GHG emission reductions or offsets as an alternative to compliance or enforcement actions resulting from violation of air pollution legislation (such as violations of Clean Air Act SIP requirements), or as an alternative for possible regulation of GHG emissions.

BAU Policy/Program:   	CA-CP program highlights include MOU’s with Star supermarket, Timberland company, Tom’s of Maine, Oakhurst Dairy, Poland Spring, York hospital

LD845 Climate Change:  This bill requires new sources of greenhouse gases to be reported to the Department of Environmental Protection. The bill also requires the department to enter into carbon emission reduction agreements with nonprofit organizations and businesses.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Measure: | BFM 5.1 Government Agency Requirement and Goals |
| --- | --- |

# Sector:	Comprehensive

Policy Description:	Energy efficiency (covered in Shared Savings Programs), Renewable Energy requirement/goal, procurement of environmentally sound services or products, recycling, etc.

BAU Policy/Program:   	EE goal of 25% below 1998 levels by 2010 (see above); Clean Government Initiative (DAFS, DEP) to procure EE appliances and equipment

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# What additional requirements and goals does the workgroup have in mind for gov’t agencies?

| Measure: | BFM 5.2 Public Benefit Fund |
| --- | --- |

# Sector:	Residential, Commercial, Industrial

Policy Description:	Surcharge on electricity and/or fossil fuel provides funding for EE measures

# BAU Policy/Program:	Efficiency Maine is funded by electricity consumers and administered by the Maine Public Utilities Commission (current funding level ~$16 million per year); no sunset date

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Electricity |  |  |
| Funds collected beyond BAU 2005-2020 | $ 15 Million | Estimated |
| Savings per $ | 2.83 kWh/$ | CT SBF Program |
| Lifetime of savings | 20 years | VT Gas program |
| Natural Gas |  |  |
| Funds collected beyond BAU 2005-2020 | $5 Million | Estimated based on CT proposal |
| Average Savings per $ for first year | 1MCF/ $29 | VT gas program |
| Lifetime of savings | 20 years | VT gas program |
| Oil |  |  |
| Funds collected beyond BAU 2005-2020 | $10 Million | Estimated based on CT proposal |
| Savings per $ | 1 MCF/$29 | VT gas program |
| Lifetime of Savings | 20 years | VT gas program |

| Measure: | BFM 5.3 Educate residents/public/children |
| --- | --- |

# Sector:	Residential

Policy Description:	Introduce energy efficiency and global warming into school curriculum, see measure “Education to homeowners” above.

BAU Policy/Program:	Maine Energy Education Program (MEEP) - provides funding for K-12 energy education programs; Maine energy curriculum investigation-allows task force of professional educators to develop improved energy education curriculum for use in Maine schools.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates: