Maine Greenhouse Gas Action Plan Development Process

Buildings, Facilities & Manufacturing Processes Greenhouse Gas Reduction Options

Center for Clean Air Policy

February 19, 2004

Contents										Page

- Overview…………………………………………………...………..2

- Preliminary GHG Savings & Cost Estimates for Priority              Measures --Edited 2-19-04………………………………………….3

- BFM Assumptions – Edited 2-19-04……………………..………....5

- BFM Emission Factors, Avoided Costs, and Discount Rates…..…..44

1.  Overview

Based on input received at the BFM Work Group Meeting held on January 23, 2004, CCAP revised preliminary GHG savings and cost estimates (see Section 2) for the priority measures identified from the 12/17 Stakeholder meeting and new options recommended by the BFM WG on 1/23.  In addition, CCAP updated the BFM assumptions document, which identifies the underlying data sources and assumptions used to develop the preliminary GHG savings and cost estimates (Section 3).  Updates to the documents are denoted with yellow highlighting.  Section 4 highlights the emission factors, avoided costs, and discount rates used in the analysis.

- Preliminary GHG Savings & Cost Estimates for Priority Measures (Page 1 of 2)

# Preliminary GHG Savings & Cost Estimates for Priority Measures, (Page 2 of 2)

# 3.  BFM Assumptions

Appliances

BFM 1.1  Energy Efficiency Appliance Standards	7

Residential

BFM 2.1  Improved Residential Building Energy Codes	8

BFM 2.2  Training and Enforcement of Building Energy Codes	10

BFM 2.3 Voluntary Green Building Design Standards	11

BFM 2.4 Energy Efficiency Mortgages	13

BFM 2.5  Education to homeowners	15

BFM 2.6  Efficient Use of Oil and Gas:  Home Heating	16

Commercial

BFM 3.1 Green standards for New construction/Renovations:State-funded Buildings	18

BFM 3.2  Incentive Payment for Green Buildings	19

BFM 3.3 State-wide EE Goals and Reporting for Government Buildings	20

BFM 3.4 Shared Savings Program for Government Agencies	21

BFM 3.5 Load Management	23

BFM 3.6 Green Campus Initiatives	24

BFM 3.7  Improved Commercial Building Energy Codes	25

BFM 3.8 HVAC Efficiency	26

Industrial

BFM 4.1 Financial Incentives for Industrial EE	27

BFM 4.2 Participate in Voluntary Industry-Government Partnerships	30

BFM 4.3 Leak Reduction Programs	31

BFM 4.4  Substitution of High GWP Gases	32

BFM 4.5 Industrial ecology/by-product synergy	34

BFM 4.6 Negotiated Agreements	35

BFM 4.7  Encourage Combined Heat and Power	36

Comprehensive

BFM 5.1  Government Agency Requirement and Goals	38

BFM 5.2  Public Benefit Fund	39

BFM 5.3  Educate residents/public/children	40

BFM 5.4  Incentives for Green Power Purchase	41

BFM 5.5  R&D for new technology	42

BFM 5.6  Wood Product Sequestration	43

| Measure: | BFM 1.1 Energy Efficiency Appliance Standards |
| --- | --- |

# Sector:			Residential, Commercial

Policy Description:	For appliances not covered under federal standards, the state can set minimum levels of efficiency for specific appliances.

# BAU Policy/Program:	Legislation proposed, never passed.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Set minimum efficiency standards for the following products:

| Product | Unit Sales in ME * (Number of Units) | Savings in 2010 (GWh or BBtu) | Savings in 2020 (GWH or BBtu) | Unit Savings (kWh or therm) | Lifetime (years) | Incremental Cost ($) |
| --- | --- | --- | --- | --- | --- | --- |
| Dry type transformers |  | 6.9 | 19.3 | 16.6 | 30 | 9 |
| Commercial refrigerators & freezers |  | 1.2 | 2 | 1542 | 9 | 115 |
| Exit signs |  | 3.7 | 10.3 | 223 | 2.5 | 30 |
| Traffic signals |  | 1.7 | 3.1 | 431 | 15 | 125 |
| Torchiere lamps |  | 66.9 | 121.7 | 288 | 10 | 40 |
| Set-Top boxes |  | 96.7 | 96.7 |  |  |  |
| Unit heaters (therm savings) |  | 68.3 | 179.7 | 268 | 18 | 425 |
| Commercial Clothes Washers |  | 1.2 | 1.8 | 197 | 8 | 200 |

Source: ENE, Communication with M Stoddard; NEEP, 2003

*Needs to be updated: Waiting for info from WG

# WG members had better data for these, but it has not yet been received.

# All of these appliances can be regulated by the state, and do not require a federal waiver.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | <0.01 | <0.01 |
| Indirect Emission Reductions (‘000 MTCO2)* | 48.4 | 68.4 |
| Total Emission Reductions (‘000 MTCO2) | 48.4 | 68.4 |
| Cost Effectiveness ($/MTCO2) |  | -285 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 2.1 Improved Residential Building Energy Codes |
| --- | --- |

# Sector:	Residential

Policy Description:	Require buildings to meet the most recent energy code efficiency/performance standards established by the International Code Council.  Continually adopt new energy codes as they are developed.

BAU Policy/Program:	Residential: State-developed code, less stringent than 1992 MEC, mandatory statewide; Voluntary IECC 2000

Maine has held four meetings of the Building Code Working Group starting in March 2003. The purpose of this group is to 1.) Survey stakeholders and determine where they stand on the issues 2.) Determine which code, NFPA or ICC, to adopt 3.) Make recommendations on how the chosen code is going to be implemented and enforced. (Source: www.bcap-energy.org)

DPUC Working Group also.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

- Residential building energy codes are updated every 3 years and adopted by ME 18 months thereafter.

# Each building energy code revision achieves the same percentage of savings.

# Includes BFM 2.2 Training and Enforcement of Building Energy Codes

| Data Need | Assumption | Source |
| --- | --- | --- |
| Energy Savings |  |  |
| Fossil Fuel savings per home (IECC 2000 compared to current construction in ME) | 10% | David Weitz, Building Code Assistance Project for Maine PUC public hearing on Nov 25th 2003 |
| # of new residential buildings built each year | 6,760 single family homes | Maine-specific data from National Association of Home Builders |
| # of residential buildings that comply with new codes | 70% | Estimated |
| Costs |  |  |
| New residential energy codes | NA |  |
| Increased cost for enforcement | $150,000 | Estimate |
| Increased cost for training | $200,000 | Based on programs in Texas and New Hampshire that provide training on residential codes and produce and distribute video recordings |

# NA:  Data not available at this time

Potential Barriers/Issues:  Avoid conflict with building rehab code

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 17.8 | 46 |
| Indirect Emission Reductions (‘000 MTCO2)* | 0.3 | 0.8 |
| Total Emission Reductions (‘000 MTCO2) | 18.1 | 46.9 |
| Cost Effectiveness ($/MTCO2) |  | -46 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 2.2 Training and Enforcement of Building Energy Codes |
| --- | --- |

# Sector:	Residential, Commercial

Policy Description:	Building codes are not effective unless implemented.  Train builders, code officials, architects, etc. on building codes

BAU Policy/Program:	Maine DPUC has joined with NEEP’s “Northeast Regional Building Energy Codes Project” to enforce building codes.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Included under BFM 2.1 Improve Residential Building Energy Codes, and BFM 3.7 Improve Commercial Building Energy Codes

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) |  |  |
| Indirect Emission Reductions (‘000 MTCO2)* |  |  |
| Total Emission Reductions (‘000 MTCO2) |  |  |
| Cost Effectiveness ($/MTCO2) |  |  |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 2.3 Voluntary Green Building Design Standards |
| --- | --- |

# Sector:	Residential

Policy Description:	Create voluntary high efficiency and sustainable building standards that builders can follow (e.g., Energy Star).

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| # of new homes built in ME | 6,760 single family homes | Maine-specific data from National Association of Home Builders |
| # of new homes meeting higher standard | 10% per year | Estimated |
| Duration of Program | 10 years |  |
| Savings between Energy Star and standard construction (based on 1992 Code Standards) | 30% | EPA |
| Incremental Cost between Energy Star and standard construction (based on 1993 MEC) | $2150/home | EPA. Note: Price varies depending on house size, prevailing construction practices, availability of equipment, etc. For example, an Energy Star labeled home can actually be less expensive to build than its non-Energy Star counterpart (i.e., good insulation, high performance windows, etc. can lower the heating and cooling loads so much that smaller and less expensive HVAC equipment and more compact duct runs are able to be installed, saving significant first costs.) |

# Owning (i.e., mortgage amortization) and operating (i.e., utility bills) an Energy Star labeled home costs less than owning and operating a non-Energy Star labeled home.  This is because we do not recommend energy-saving measures unless the amortized cost of implementing those measures is less than the utility bill savings resulting from them.  Source:  EPA Energy Star Homes

# GHG emission savings are estimated assuming BFM 2.1 is not implemented.  If implemented, GHG emission savings will be decreased.

# Note:  This option may potentially be funded through BFM 5.2.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 7.8 | 14.2 |
| Indirect Emission Reductions (‘000 MTCO2)* | 2.4 | 4.4 |
| Total Emission Reductions (‘000 MTCO2) | 10.2 | 18.6 |
| Cost Effectiveness ($/MTCO2) |  | -64 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 2.4 Energy Efficiency Mortgages |
| --- | --- |

# Sector:	Residential

Policy Description:	1) Recommend that the PUC's Efficiency Maine Program take steps to promote Energy Efficient Mortgages (EEMs) to Maine home buyers and homeowners that qualify. An EEM is a mortgage where the cost of installing “cost effective” energy improvements can be included in the total amount being financed (or refinanced) in any HUD/FHA, VA, or Fannie Mae mortgage. Homebuyers can generally finance from $3,000 to $8,000 worth of energy improvements directly into their mortgage so long as a Home Energy Rating System (HERS) Provider documents that the expected average monthly energy savings will be greater than the small amount added to the monthly mortgage payment to cover the $3,000 to $8,000 EEM. In Maine and New Hampshire, almost every home can gain significant energy savings from just a few hundred to a few thousand dollars worth of “targeted” energy improvements.  This measure applies to both new and existing homes. (http://www.horizon-res.com/EEMs.htm).

2) Support the recommendation of the housing roundtable to make Location-Efficient Mortgages SM (LEM) available in Maine. From a roundtable discussion on housing issues for Maine's Congressional Delegation to consider, Portland, August 5, 2003:  Expand the availability of the Location Efficient Mortgage SM  (LEM). Now offered by Fannie Mae only in Seattle, San Francisco, Los Angeles, and Chicago, LEMs increase the borrowing power of homebuyers by up to 30% by taking into account the money they save by living in urban neighborhoods where they can walk, bicycle, or use public transit. In Southern Maine, LEMs would enable young families earning 80% of median to qualify for homes in Portland, South Portland, and Westbrook, which range from $170,000-$190,000, instead of lower priced homes in rural areas, such as Gray or Hollis, which range from $144,000-$160,000. (http://216.239.37.104/search?q=cache:MWd75fm6TrIJ:www.nhc.org/yrendrtb03portlandme.pdf+Location+Efficient+Mortgage+%2B+Maine&hl=en&ie=UTF-8)

BAU Policy/Program:	EEMs are available in Maine, but it is likely that they are not yet widely understood, marketed, or sold.  Location Efficient Mortgages are not currently offered in Maine. Location Efficient Mortgage services are available in the cities of Chicago and Seattle; Los Angeles County; and the nine-county San Francisco Bay Area. The mortgage services are currently part of an underwriting experiment sponsored by Fannie Mae.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Energy Efficiency Mortgages |  |  |
| Average annual energy savings per home |  |  |
| Electricity | 3% | Energy Rated Homes of VT |
| Fossil Fuel | 39% | Energy Rated Homes of VT |
| # of homes resold each year in ME | 13,246 | Maine Real Estate Information System (MREIS) |
| # of home buyers participating in Mortgage Program | 1% | Estimate |
| Cost of implementing program | $2353/home | Fannie Mae |

# NA: Data not currently available.

Calculating Savings for Location Efficient Mortgages:  By drawing on land-use information such as population density and public transit locations, and census information on car ownership and driving levels, a lender can predict how much a household in a particular location will spend on transportation. Based on this prediction, the lender calculates the difference in transportation costs between an urban household and its suburban counterpart. This dollar amount is then added onto the buyer's qualifying income. The amount can be substantial, as it takes into account savings on vehicle purchases and maintenance, auto insurance, and fuel (the formula for calculating these savings was developed specifically for the Location Efficient Mortgage® program). (Source: NRDC)  Note Coordinate with Transportation Working Group to develop GHG estimates and costs.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 2.0 | 4.9 |
| Indirect Emission Reductions (‘000 MTCO2)* | 0.1 | 0.2 |
| Total Emission Reductions (‘000 MTCO2) | 2.0 | 5.1 |
| Cost Effectiveness ($/MTCO2) |  | -19 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 2.5 Education to homeowners |
| --- | --- |

# Sector:	Residential

Policy Description:	Educate homeowners on EE and sustainable design retrofits, renovations and new construction options (e.g., provide EE education materials at time of resale or refinancing).

BAU Policy/Program:	Education programs under Efficiency Maine; Programs by DEP

There are two energy education programs operating in Maine. One program, the Maine Energy Education Program (MEEP), provides education on energy is-sues to kindergarten through twelfth grade students in the Bangor Hydro-Electric and Central Maine Power service territories. A second program, operated by Maine Public Service Company, offers educational pro-grams in the Maine Public Service territory. Both programs strive to increase consumer knowledge of energy efficiency - a fundamental market barrier to economically efficient behavior. (Anticipated budget 2004: $417,560)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# What type of program is envisioned?

# When/Where/How would homeowners be targeted?

# During building inspection at time of resale

# Mandatory efficiency ratings on furnaces/boilers/other equipment

# Through electricity billing

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 2.6 Efficient Use of Oil and Gas: Home Heating |
| --- | --- |

# Sector:	Residential

Policy Description:	Provide incentives for EE retrofits or upgrades for home heating equipment, hot water heaters, programmable thermostats

BAU Policy/Program:	LIHEAP, WAP, REACH Central Heating Improvement (CHIP) Programs for low-income residents. (Energy Advisors, LLC, 2003)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Sources |
| --- | --- | --- |
| Oil Furnaces/Boilers |  |  |
| # operating at or below 60% AFUE | 15% | Expert judgement |
| Energy savings associated with replacing 60% AFUE furnace with Energy Star oil Furnace (90% AFUE) | 24.25 MMBTU/furnace | Calculated based on 30% efficiency increase and avg 80.8 MMBTU/household for space heating |
| Estimated cost of conventional oil furnace | $2000 | EPA |
| Estimated cost of Energy Star oil furnace | $2700 | Consumer Energy Council of America (2001) |
| Market penetration | 2% | Estimated |
| Natural Gas Furnaces |  |  |
| # operating at or below 60% AFUE | 15% | Expert Judgement |
| Energy savings associated with replacing 60% AFUE furnace with Energy Star natural gas furnace (90% AFUE) | 24.25 MMBTU/furnace | Calculated based on 30% efficiency increase and avg 80.8 MMBTU/household for space heating |
| Estimated cost of conventional natural gas furnace | $2000 | EPA Energy Star |
| Estimated cost of Energy Star natural gas furnace | $2500 | EPA Energy Star |
| Market Penetration | 2% | Estimated |
| Integrated hot water heater |  |  |
| Average energy factor of stand alone water heater more than 10 years old | 50% | USDOE Building Technologies Program |
| Energy factor of new integrated hot water heater | 88% | USDOE Building Technologies Program |
| Cost of installation | 900 | USDOE Building Technologies Program |
| Market Penetration | 2% of oil heated homes; 2% natural gas heated homes | Assume install with furnace replacement |
| Set-back Thermostat |  |  |
| Energy Savings per year | 5% | EPA (Ranges from 5 to 30%)- Energy Star requires 2 programs with 4 settings each |
| Cost | $195 | EPA (product cost ranges from 40-120; installation charge of 25-75) |
| Market Penetration | 2% of oil heated homes; 2% natural gas heated homes | Assume install Energy Star Programmable Thermostat with boiler replacement |
| Percentage of Homes by Heating Fuel Type |  |  |
| Oil | 80% | US Census, 2000 |
| Natural Gas | 8% | US Census, 2000 |
| Electricity | 4% | US Census, 2000 |
| Number of homes in ME | 518,200 | US Census, 2000 |

- Note:  This option may potentially be funded through BFM 5.2.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 26.1 | 34.7 |
| Indirect Emission Reductions (‘000 MTCO2)* | 0.0 | 0.0 |
| Total Emission Reductions (‘000 MTCO2) | 26.1 | 34.7 |
| Cost Effectiveness ($/MTCO2) |  | 4 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.1 Green standards for New construction/Renovations: State-funded Buildings |
| --- | --- |

## Sector:	Commercial

Policy Description:	New construction as well as major renovations of all building projects that receive some state funding (state facilities, local schools, etc.) should be required to be at least 30% more efficient than required by the state energy codes.

BAU Policy/Program:	The State of Maine has recently passed two pieces of legislation regarding this issue:  1) The Development of optimal energy efficiency in state state-funded construction (requires buildings be designed and built to standards of energy efficiency that are always at least 30% higher than the minimum energy standard s required by current state energy codes), and 2) Construction of schools (amends rules on construction of new schools to require that all construction proposals must be based on the most energy and environmentally efficient designs suitable).

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumptions | Sources |
| --- | --- | --- |
| Total Sq ft of state-funded buildings built each year | 525,000 | Placeholder, Waiting for data from Maine Bureau of General Services |
| Requirement by State of Maine for energy savings compared to minimum energy standards | 30% | Maine EO |
| Average energy intensity for government buildings |  |  |
| Electricity | 12.9 kWh/sq ft | EIA CBECS (1999) |
| Natural Gas | 28.7 cu ft/sq ft | EIA CBECS (1999) |
| Oil | 0.2 gallons/sq ft | EIA CBECS (1999) |
| Incremental cost | $4/sq ft | Kats et al. (2003) |

NA: Data not available

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 2.0 | 5.3 |
| Indirect Emission Reductions (‘000 MTCO2)* | 3.3 | 8.7 |
| Total Emission Reductions (‘000 MTCO2) | 5.3 | 14 |
| Cost Effectiveness ($/MTCO2) |  | -30 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.2 Incentive Payment for Green Buildings |
| --- | --- |

## Sector:	Commercial

# Policy Description:	Encourage privately financed new construction and renovation to be high performance buildings by certifying to LEED standard.

# Provide tax credits and other financial incentives for green buildings, similar to those offered in NY and MA.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Number of commercial buildings built each year | 2,184 | CT data scaled to ME. Placeholder- source for data? |
| Market penetration | 2% | Estimate |
| Energy Savings for LEED Silver compared with 1989 Building Code | 0-30% GHG estimate based on 30% | Steven Winters Associates; LEED Silver does not ensure that there will be an improvement in the EE of the building (D Baston) |
| Average energy intensity for non-government buildings |  |  |
| Electricity | 13.4 kWh/sq ft | EIA CBECS (1999) |
| Natural Gas | 43.1 cu ft/sq ft | EIA CBECS (1999) |
| Oil | 0.18 gallons/sq ft | EIA CBECS (1999) |
| Incremental Cost | $4/sq ft | Kats et al. (2003) |

Note:  This option may potentially be funded through BFM 5.2.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 2.11 | 5.6 |
| Indirect Emission Reductions (‘000 MTCO2)* | 4.3 | 11.3 |
| Total Emission Reductions (‘000 MTCO2) | 6.4 | 16.9 |
| Cost Effectiveness ($/MTCO2) |  | -35 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.3 State-wide EE Goals and Reporting for Government Buildings |
| --- | --- |

# Sector:	Commercial/Government Agency Buildings

Policy Description:	A program to encourage measurement and tracking of energy consumption, strategic planning, and benchmarking against other buildings.

BAU Policy/Program:	 25% energy reduction goal by 2010 (relative to 1998 baseline) added to Energy Conservation Building Act for Public Buildings. This legislation established a pilot program to seek to achieve that level of energy savings in ten facilities of over 40,000 square feet. Under the pilot program, energy savings are to be achieved through performance contracts with energy service companies.

LD845 Climate Change:  This bill requires new sources of greenhouse gases to be reported to the Department of Environmental Protection.  It also requires the department to create an inventory of greenhouse gas emissions associated with state-owned facilities and state-funded programs and to create a plan for reducing those emissions.

The Maine Public Utilities Commission and the Maine Department of Administrative and Financial Services

(DAFS) developed a Memorandum of Understanding (MOU) to improve the energy efficiency of State buildings. The program will fund renovations that enhance electrical efficiency. It will also fund an energy survey of all state buildings to identify opportunities for energy efficiency. Under the MOU, DAFS identifies potential projects and Efficiency Maine reviews the proposed projects for cost effectiveness. If the projects are

cost effective, they are developed and managed by DAFS and financed through the funds administered by Efficiency Maine.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

- Savings will show up under BFM 3.4.  Benchmarking will help to identify which buildings to pursue first

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.4 Shared Savings Program for Government Agencies |
| --- | --- |

# Sector:	Commercial/Government Agency Buildings

Policy Description:	Incentive program for state agencies achieving savings through energy conservation, with portion of savings retained by agency for future energy costs/activities.

BAU Policy/Program:	Under a law passed in 1991, the Bureau of Public Improvements (predecessor to the Bureau of General Services) was charged with developing a program “in which an eligible department or agency of the State may retain a portion of any first-year energy cost savings demonstrably attributable to energy efficiency improvements undertaken by that department or agency.”105 The Bureau was required to submit the proposed program to the legislative Committee on State and Local Government by January 1, 1992. It does not appear that this program was ever implemented. (Energy Advisors, LLC, 2003)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| State Agency Fuel Consumption |  |  |
| Electricity | 127,384 MWh | Energy Advisors, LLC |
| Natural Gas | 90,025 MMBTU | Estimated using government to commercial sector electricity share |
| Oil | 643,062 MMBTU | Estimated using government to commercial sector electricity share |
| Government building share of commercial sector electricity consumption | 3% | Energy Advisors, LLC |
| Reduction in state energy use by 2010 | 20% | Estimated |
| Reduction in state energy use by 2020 | 50% | Estimated |
| Costs | $0.3/kWh | Placeholder: based on Maine Efficiency results from state building program |

NA: Data not available

Note:  This option may potentially be funded through BFM 5.2.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 10.9 | 26.4 |
| Indirect Emission Reductions (‘000 MTCO2)* | 7.3 | 17.4 |
| Total Emission Reductions (‘000 MTCO2) | 18.1 | 43.8 |
| Cost Effectiveness ($/MTCO2) |  | -110 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.5 Load Management |
| --- | --- |

# Sector:	Commercial

# Policy Description:	Overcome existing regulatory barriers to increase the market diffusion of third party load management for non-intrusive commercial loads (e.g., dimming lights, planned cycling of refrigeration compressors)

## BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Market Size | 1250 MW | Scaled CT market size to ME based on share of commercial electricity consumption |
| Market Penetration per year | 5% | Estimated |
| Incremental Cost | $500/kW | NXEGEN |

NA: Data not available at this time

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 0.0 | 0.0 |
| Indirect Emission Reductions (‘000 MTCO2)* | 2.9 | 4.7 |
| Total Emission Reductions (‘000 MTCO2) | 2.9 | 4.7 |
| Cost Effectiveness ($/MTCO2) |  | -220 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.6 Green Campus Initiatives |
| --- | --- |

Sector:	Commercial

Policy Description:  	Promote a “Green Campus” Initiative with all Maine Colleges, Universities, Private/Secondary Schools with Campus to minimize environmental impact

# BAU Policy/Program:  	Currently underway

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Duration of Proposed Program | 5 years | Estimated |
| Market Size | 27 colleges and universities with 52,441 student enrollment | Department of Education |
| Average $/student for energy | $265/Student | Based on University of Southern Maine |
| % of Market enrolled in program each year | 5% | Estimated |
| Average electricity savings | 15% | Communication with Clean Air-Cool Planet |
| Average fossil fuel reductions | 10% | Communication with Clean Air-Cool Planet |
| Cost | $0.3/kWH | Place holder based on Efficiency Maine State Building Program |

Note:  This option may potentially be funded through BFM 5.2.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 6.5 | 20.6 |
| Indirect Emission Reductions (‘000 MTCO2)* | 1.6 | 4.9 |
| Total Emission Reductions (‘000 MTCO2) | 8.1 | 25.5 |
| Cost Effectiveness ($/MTCO2) |  | -224 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.7 Improved Commercial Building Energy Codes |
| --- | --- |

# Sector:	Commercial

Policy Description:	Require buildings to meet the most recent energy code efficiency/performance standards established by the International Code Council. .

BAU Policy/Program:	Commercial: ASHRAE/IESNA 90.1-2001, mandatory statewide; can COM check -EZ to show compliance (Most up to date).  Automatic adoption of commercial building energy codes.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Included in baseline as legislation requires automatic upgrade of ASHRAE Standards.

| Data Need | Assumption | Source |
| --- | --- | --- |
| Annual Commercial Savings |  |  |
| Oil savings | NA |  |
| Natural gas savings | NA |  |
| Electricity savings | NA |  |
| New commercial buildings built each year | 2,184 | CT data scaled to ME |
| Number of commercial buildings that comply with new codes | 70% | Estimated |
| Costs |  |  |
| Cost for new commercial building code | NA |  |
| Cost for enforcement | NA |  |
| Cost for training | NA |  |

# NA:  Data not available at this time

Potential Barriers/Issues:  Avoid conflict with Rehab code

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.8 HVAC Efficiency |
| --- | --- |

Sector:	Commercial

Policy Description:  	 Two sources of energy savings include (1) computer technology to regulate system and (2) significant energy management initiatives.

# BAU Policy/Program:  	 Efficiency Maine C&I Program, available to businesses with > 50 FTEs, includes three components (1) business practices training, (2) information and end-use training opportunities, and (3) financial grants to assist in the purchase of EE equipment.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Savings associated with installing HVAC computer technology (based on adaptative/fuzzy logic control) | 5% | DOE Buildings Technology Program |
| Commercial Building Energy Used for HVAC as percentage of primary energy use | 30% | DOE Buildings Technology Program |
| Market penetration | NA |  |
| Costs associated with installing computer technology | NA |  |

NA: Data not available

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.1 Financial Incentives for Industrial EE |
| --- | --- |

# Sector:	Industrial

Policy Description:	Offer financial incentive/rebates for EE improvements taken at ME industries

# BAU Policy/Program:	Efficiency Maine has established a new Commercial and Industrial Program for Maine businesses that provides a combination of services, including energy efficiency information and training, business practice assistance, and direct financial incentives in the form of grants. The components of the program are designed to encourage businesses to adopt energy efficient business practices, to include consideration of energy costs and energy efficiency in their business decisions, and to purchase and install energy efficient products.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Performance of Efficiency Maine’s C&I program | 10 kWh/$ | CT’s Energy Opportunities program; up to 30% cost share |
| Level of increased funding | $2 million | Estimate |

# Note:  This option may potentially be funded through BFM 5.2.

# Many states have provided financial incentives for energy savings in the private sector. Efficiency incentives primarily appear in one of three forms- grants, loans and tax incentives.

| Financial Incentive | Example |
| --- | --- |
| Corporate tax incentives | The Maryland Clean Energy Incentive Act provides Maryland sales tax exemptions or income tax credits when purchasing certain qualifying high efficiency Energy Star appliances, electric and hybrid-electric vehicles, and certain renewable resource energy systems. The Act also provides for a personal or corporate income tax credit for the production of electricity from commercial and industrial waste, forestry (excluding old growth residue) and agricultural by-products, and landfill and anaerobic digestion biogas. The credit is 0.85¢/kWh (or 0.5¢/kWh for electricity generated in a co-fired plant). The electricity must be sold to an unrelated party to take advantage of the credit. The unused amount of the credit may be carried forward and applied for succeeding taxable years for up to ten years. (Website: http://www.energy.state.md.us/programs/cleanincentives.html ) |
| Property Tax Reduction | Montana generating plants producing 1 megawatt or more by means of an alternative renewable energy source are eligible for the new or expanded industry property tax reduction on the local mill levy during the first nine years of operation, subject to approval by the local government. If so approved, the facility is taxed at 50 percent of its taxable value in the first five years after the construction permit is issued. Each year thereafter, the percentage is increased by equal percentages until the full taxable value is attained in the tenth year. (Website: http://www.deq.state.mt.us/energy/Renewable/TaxIncentRenew.asp#15-24-1401) |
| Business Energy Tax Credit | Oregon Department of Energy: Tax credit to those who invest in energy conservation, recycling, renewable energy resources and less-polluting transportation fuels. The tax credit is 35 percent of the eligible project costs - the incremental cost of the system or equipment that's beyond standard practice. You take the credit over five years: 10 percent in the first and second years and 5 percent each year thereafter. If you can't take the full tax credit each year, you can carry the unused credit forward up to eight years. Those with eligible project costs of $20,000 or less may take the tax credit in one year. http://www.energy.state.or.us/bus/tax/taxcdt.htm |
| Cash Incentives | In cooperation with Narragansett Electric Small Business Program, The Rhode Island State Energy Office, (RISEO) is providing cash incentives to small commercial/industrial applicants (<100KW per month) who install high-efficiency heating equipment measures (e.g., temperature control, EMS, steam trap replacement, boiler reset controls, etc.). All incentives capped at 25% of installed cost or $3,000 per building, whichever is lower. Oregon’s Industrial Energy Savings Plan (ESP) offers cash incentives for industrial facilities and manufacturing processes to improve their energy efficiency. Typical opportunities include building and process controls, adjustable frequency drives, compressed air systems, exhaust systems, material handling systems, fans and pumps, lighting, and process efficiency improvements. Incentives are based on the measured reduction in energy use resulting from installing energy-efficient equipment instead of standard equipment in new installations. Incentives are paid following project completion, commissioning and verification of energy savings. (Source: EWEB) Entergy’s Large C&I program offers incentives for demand savings and/or energy savings. The incentive prices may not exceed 35% of the avoided costs of supplying electricity (e.g., $164/kW or $0.056/kWh). |
| Zero/Low Interest Loan Program | Indiana’s Industrial Energy Efficiency Fund is a zero-interest loan program geared to help manufacturers increase the EE of their manufacturing process. The fund is used to replace or convert existing equipment, or to purchase new equipment as part of a process/plant expansion, which will lower energy use. Companies can receive as much as $250,000. (Potential in Maine under FAME?) |
| Rebates | EWEB Energy-Efficient Motor Program offers rebates to EWEB's commercial and industrial customers for purchasing energy- efficient, three-phase electric motors between three horsepower and 500 horsepower. To be eligible, motors must be meet minimum nominal full load efficiencies published by EWEB and must be installed or inventoried within EWEB's service territory. The rebate is available either from participating motor suppliers as a discount on the motor sales price at the time of purchase or from EWEB as a cash payment after the motor is purchased. |
| Bonds | Bonds provide up-front capital by attracting investment in the credit-worthiness of an institution |

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 0 | 0 |
| Indirect Emission Reductions (‘000 MTCO2)* | 32.6 | 85.8 |
| Total Emission Reductions (‘000 MTCO2) | 32.6 | 85.8 |
| Cost Effectiveness ($/MTCO2) |  | -209 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.2 Participate in Voluntary Industry-Government Partnerships |
| --- | --- |

## Sector:	Commercial, Industrial

Policy Description:	Strongly promote voluntary programs and actions to the appropriate sectors. While some programs already exist at the national level, there may also be an opportunity to develop additional programs in Maine.

BAU Policy/Program:   	Several programs already exist at the national level:  EPA Climate Leaders, DOE Industries of the Future (Maine Industries of the Future currently includes pulp and paper, secondary wood, and metals industry), EPA Energy Star Benchmarking Program, DOE Rebuild America; Maine STEP-UP program, Carbon Challenge

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# DOEs suggestions for expanding Maine participation in IOF:

# Include agriculture and plastics and potentially welding

# Additional publicity

# The Maine legislature might consider creating a mini state grant program that could provide funds to Maine businesses for feasibility studies to determine whether to adopt new energy-efficient technologies.

# Discuss energy and EE technologies as part of technology cluster project

# The Maine Smart Tracks for Exceptional Performers and Upward Performers, or STEP-UP, Program offers recognition and other incentives to businesses interested in implementing sustainable practices.

# Alan Auto (Portland), Bath Iron Works (Bath), Fairchild Semiconductor (South Portland), Interface Fabrics Group (Guilford), Moss, Inc. (Belfast), NorDx (Scarborough) and Poland Springs Bottling Company (Hollis). College of the Atlantic (Bar Harbor), CYRO Industries (Sanford), National Semiconductor of Maine (South Portland) and Naturally Potatoes (Mars Hill).

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.2 Leak Reduction Programs |
| --- | --- |

# Sector:	Industrial

Policy Description:	Reduce methane leaks from natural gas systems, reduce HFC leaks from refrigeration, motor vehicle air conditioning, etc.

BAU Policy/Program:   	Existing federal programs to reduce methane leaks from natural gas pipelines, SF6 from electricity substations

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Increased participation in EPA Natural Gas Star | NA |  |
| Increased participation in SF6 Electrical Utility | NA |  |
| ODS substitute emissions from refrigeration and A/C | 67% | US EPA based on national statistics |
| HFC emissions from stationary refrigeration | 40% | USEPA based on national statistics |
| Market penetration | 5% per year | Estimated |
| HFC leak reduction potential for stationary refrigerants | 5% | US EPA |

# NA: Data not available at this time

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 1.2 | 9.0 |
| Indirect Emission Reductions (‘000 MTCO2)* | N/A | N/A |
| Total Emission Reductions (‘000 MTCO2) | 1.2 | 9.0 |
| Cost Effectiveness ($/MTCO2) |  | 0.27 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.3 Substitution of High GWP Gases |
| --- | --- |

# Sector:	Industrial

Policy Description:	 Substituting other gases for high GWP gases is a viable option as long as environmental, health, safety, and performance requirements can be met.

BAU Policy/Program:   	None.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Alternative Refrigerants

# Ammonia. Ammonia, primarily used in water cooled chillers, has excellent thermodynamic properties and can be used in many types of systems. However, it must be used carefully, because it is toxic and slightly flammable.  Building and fire codes restrict the use of ammonia in the urban areas of the United States and many other countries. (EPA, 2001)

# Hydrocarbons. Hydrocarbons have thermodynamic properties that make them good refrigerants; however, their high flammability causes concern for safety. Hydrocarbon refrigerant use is generally restricted by U.S. safety codes, with the exception of industrial refrigeration(EPA, 2001).

# Carbon Dioxide. Carbon dioxide has been investigated for use primarily in mobile air-conditioning systems and refrigerated transport. (EPA, 2001)

# Alternative Solvent Fluids

# In electronics, metal, and some precision cleaning end uses, alternative organic solvents with lower GWPs are being manufactured and integrated into the industry. Some of these solvents, such as HFCs, HFEs, hydrocarbons, alcohols, volatile methyl siloxanes, brominated solvents, and non-ODS chlorinated solvents, can be used as alternatives to PFC/PFPEs, CFCs, and HCFCs.

# Non-HFC Blowing Agents

# Hydrocarbons (HC) Hydrocarbons such as propane and butane are alternatives to HFCs. HCs are inexpensive and have lower GWP impacts relative to HFCs. However, key technical issues associated with hydrocarbons are: flammability, VOCx, and performance.

# Liquid Carbon Dioxide (LCD).  Foams blown with CO2 might suffer from lower thermal conductivity, lower dimensional stability, and higher density versus HCFC blown foams. To overcome these limitations, CO2 can be blended with hydrocarbons or HFCs.

# Water-Blown (in situ) Carbon Dioxide (CO2/water).  During manufacturing, no ODP or high GWP gases are emitted, and there are limited  health and safety risks during processing. However, foams produced using CO2/water are subject to the same performance limitations discussed for LCD-blown foams

# Lower-GWP HFC Substitution.  Manufactures can reduce their emissions on a carbon basis by switching from a blowing agent with a high GWP to one with a lower GWP, but any associated energy penalties must also be considered.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

# * Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.4 Industrial ecology/by-product synergy |
| --- | --- |

# Sector:	Industrial

Policy Description:	Programs to link the by-products from one industry with use as the feedstock for other industries.

BAU Policy/Program:   	None.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

No data available

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.5 Negotiated Agreements |
| --- | --- |

# Sector:	Industrial

Policy Description:	To promote GHG reductions in particular sectors, a state government may enter into direct voluntary or negotiated agreements with industries or industrial sectors. Negotiated agreements, for example, would result in agreed-upon GHG emission reductions or offsets as an alternative to compliance or enforcement actions resulting from violation of air pollution legislation (such as violations of Clean Air Act SIP requirements), or as an alternative for possible regulation of GHG emissions.

BAU Policy/Program:   	CA-CP program highlights include MOU’s with Star supermarket, Timberland company, Tom’s of Maine, Oakhurst Dairy, Poland Spring, York hospital

LD845 Climate Change:  This bill requires new sources of greenhouse gases to be reported to the Department of Environmental Protection. The bill also requires the department to enter into carbon emission reduction agreements with nonprofit organizations and businesses.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.6 Encourage Combined Heat and Power |
| --- | --- |

# Sector:	Industrial

Policy Description:	Combined heat and power (CHP) is the simultaneous production of electricity and heat using a single fuel. The heat produced from the electricity generating process is captured and utilized to produce high and low level steam. The steam can be used as a heat source for both industrial and domestic purposes and can be used in steam turbines to generate additional electricity (combined cycle power).

BAU Policy/Program:   	CHP units are included as eligible renewable sources under the state Renewable Resource Portfolio Requirement

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

For preliminary analysis, following assumptions were made:

# EEA MW potential represents technical potential only, and does not evaluate economic potential.  EEA assumes commercial units are reciprocating engines less than 5 MW, industrial units are simple-cycle combustion turbines of 5-10 MW capacity.

# Based on EGRID data, CHP capacity factor assumed to be 0.4 for commercial, 0.6 for industrial.

# CHP electric efficiency assumed to be 0.4 for both commercial and industrial.

# Power-to-heat ratio assumed to be 0.8 for all units based on units of similar capacity in EGRID.

# All CHP units assumed to be fired by natural gas.

# Fuel input of stand-alone boilers replaced assumed to be 2/3 gas, 1/3 oil (Btu basis).  Oil is assumed to be distillate fuel.

# Efficiency of stand-alone boilers assumed to be 80%.

| Data Need | Assumption | Source |
| --- | --- | --- |
| Technical potential of CHP capacity in Maine in 2010 (MW) |  |  |
| Commercial (MW) | 411 |  |
| Industrial (MW) | 232 |  |
| Total (MW) | 643 |  |
| Technical potential of CHP capacity in Maine in 2020 (MW) |  | EEA |
| Commercial (MW) | 411 |  |
| Industrial (MW) | 232 |  |
| Total (MW) | 643 |  |
| Economic potential of CHP capacity in ME | NA |  |

NA: Data not available

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) |  |  |
| Indirect Emission Reductions (‘000 MTCO2)* |  |  |
| Total Emission Reductions (‘000 MTCO2) | 365 | 355 |
| Cost Effectiveness ($/MTCO2) |  | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

# * Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 5.1 Government Agency Requirement and Goals |
| --- | --- |

# Sector:	Comprehensive

Policy Description:	Energy efficiency (covered in Shared Savings Programs), Renewable Energy requirement/goal, procurement of environmentally sound services or products, recycling, etc.

BAU Policy/Program:   	EE goal of 25% below 1998 levels by 2010 (see above); Clean Government Initiative (DAFs, DEP) to procure EE appliances and equipment

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# What additional requirements and goals does the workgroup have in mind for gov’t agencies?

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 5.2 Public Benefit Fund |
| --- | --- |

# Sector:	Residential, Commercial, Industrial

Policy Description:	Surcharge on electricity and/or fossil fuel provides funding for EE measures

# BAU Policy/Program:	Efficiency Maine is funded by electricity consumers and administered by the Maine Public Utilities Commission (current funding level ~$16 million per year); no sunset date

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Electricity |  |  |
| Funds collected beyond BAU 2005-2020 | $ 15 Million | Estimated |
| 2003 Efficiency Maine Program Costs | $2,921,000 | Efficiency Maine Annual Report 2003 |
| 2003 Annual Participant Benefits | $370,150 | Efficiency Maine Annual Report 2003 |
| Savings (1st year) | 4,837 t CO2 | Efficiency Maine Annual Report 2003 |
| Lifetime of savings | 15 years | CT C&LM Fund |
| Natural Gas |  |  |
| Funds collected beyond BAU 2005-2020 | $5 Million | Estimate |
| Average Savings per $ for first year | 1MCF/ $29 | VT gas program- Is there a better source (D Baston) |
| Lifetime of savings | 15 years | CT C&LM Fund |
| Oil |  |  |
| Funds collected beyond BAU 2005-2020 | $10 Million | Estimate |
| Savings per $ | 1 MCF/$29 | VT gas program- Is there a better source (D Baston) |
| Lifetime of Savings | 15 years | CT C&LM Fund |

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 134 | 357.2 |
| Indirect Emission Reductions (‘000 MTCO2)* | 81.5 | 201.7 |
| Total Emission Reductions (‘000 MTCO2) | 215.4 | 558.9 |
| Cost Effectiveness ($/MTCO2) |  | -529 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 5.3 Educate residents/public/children |
| --- | --- |

# Sector:	Residential

Policy Description:	Introduce energy efficiency and global warming into school curriculum, see measure “Education to homeowners” above.

BAU Policy/Program:	Maine Energy Education Program (MEEP) - provides funding for K-12 energy education programs; Maine energy curriculum investigation-allows task force of professional educators to develop improved energy education curriculum for use in Maine schools. (See also BFM 2.5)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 5.4 Incentives for Green Power Purchase |
| --- | --- |

# Sector:	Residential, Commercial, Industrial

Policy Description:	To promote and encourage the deployment of renewable energy resources in the region (beyond RPS requirements) by Maine businesses, municipalities, institutions, and households, Maine ratepayers should have the choice of determining where their power comes from through a green offering(s).

BAU Policy/Program:	Maine Renewable Energy is now offering on a limited basis to residential and small commercial customers in either the CMP or Bangor Hydro service territories electricity that is 100% renewable / 100% from Maine.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Sources |
| --- | --- | --- |
| Green power purchase goal in 2010 | 3% of total electricity demand | Estimate |
| Green power purchase goal in 2020 | 6% of total electricity demand | Estimate |
| Maine electricity demand in 2010 | 12,430,000 MWh | Maine Energy Policy Report |
| Maine electricity demand in 2020 | 13,937,000 MWh | Projection based on Maine Energy Policy Report |
| Incremental cost for RE | 0.015$/kWh | Maine Renewable Energy |

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | N/A | N/A |
| Indirect Emission Reductions (‘000 MTCO2)* | 101.4 | 224.3 |
| Total Emission Reductions (‘000 MTCO2) | 101.4 | 224.3 |
| Cost Effectiveness ($/MTCO2) |  | 56 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 5.5 R&D for new technology |
| --- | --- |

# Sector:	Residential, Commercial, Industrial

Policy Description:	R&D program for new technology

BAU Policy/Program:

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Note: Addressed by EW 7.2

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 5.6 Wood Product Sequestration |
| --- | --- |

# Sector:	Residential, Commercial, Industrial

Policy Description:	Wood Product Sequestration

BAU Policy/Program:

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Note: Addressed by AF 2.6

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

4.  BFM Emission Factors, Avoided Costs, and Discount Rate

# Footnotes

Estimate appears to be conservative based on 18% reduction cited in Xenergy (2001), “Impact Analysis of the Massachusetts 1998 Energy Code Revisions”

##### The national Home Energy Ratings System (HERS) method rates a home on a scale of 0 to 100, with 0 being the least energy efficient and 100 being a highly energy efficient house. The system is based on comparing the house being rated to a computer model of that exact same house if it were built to the national Council of American Building Officials - Model Energy Code (CABO MEC) standards for residential construction. This computer modeled house is called the "Reference House." A score of 80 would be a house which meets CABO MEC standards. If the house being rated is less energy efficient than its computer modeled Reference House, then it would score less than 80 points. If the house being rated is more energy efficient than its computer modeled Reference House, then it would score more than 80 points. An EPA Energy Star® Home is a new or energy improved home which scores 86 or higher on the HERS scale. (Five Star and Five Star Plus Homes). (Source: http://www.horizon-res.com/EEMs.htm)

LOCATION EFFICIENT MORTGAGE services is a certification mark owned by the Institute for Location Efficiency. Unauthorized use of this mark is prohibited.

“Costs and Financial Benefits of Green Buildings: A Report to California’s Sustainable Building Task Force” (October 2003). Costs based on 33 green buildings compared to conventional designs for those buildings.  The Average premium was slightly less than 2% or $3-5/sq ft.

“Costs and Financial Benefits of Green Buildings: A Report to California’s Sustainable Building Task Force” (October 2003). Costs based on 33 green buildings compared to conventional designs for those buildings.  The Average premium was slightly less than 2% or $3-5/sq ft.