Maine Greenhouse Gas Action Plan Development Process

Buildings, Facilities & Manufacturing Processes Greenhouse Gas Reduction Options

Center for Clean Air Policy

March 19, 2004

Contents										Page

- Overview…………………………………………………...………..2

- Preliminary GHG Savings & Cost Estimates for Priority              Measures --Edited 3-19-04………………………………………….3

- BFM Assumptions – Edited 3-19-04……………………..………....4

1.  Overview

Based on input received at the BFM Working Group Meeting held on February 26, 2004 and over the past month, CCAP revised preliminary GHG savings and cost estimates (see Section 2) for the priority measures identified from the 12/17 Stakeholder meeting and new options recommended by the BFM WG.  In addition, CCAP updated the BFM assumptions document, which identifies the underlying data sources and assumptions used to develop the preliminary GHG savings and cost estimates (Section 3).  Updates to the document are denoted with green highlighting.

2.  Preliminary GHG Savings & Cost Estimates for Priority Measures

# 3.  BFM Assumptions

# Table of Contents

Appliances

BFM 1.1  Energy Efficiency Appliance Standards					3

Residential

BFM 2.1  Improved Residential Building Energy Codes				4

BFM 2.2  Training and Enforcement of Building Energy Codes			6

BFM 2.3 Voluntary Green Building Design Standards				7

BFM 2.4 Energy Efficiency/Location Efficient Mortgages				9

BFM 2.5  Education to homeowners						11

BFM 2.6  Efficient Use of Oil and Gas:  Home Heating				12

Commercial

BFM 3.1 Energy standards for New Construction/Renovations			14

BFM 3.2  Incentive Payment for Energy Efficient Buildings			16

BFM 3.3 Encourage state to fund fastest most cost-effective energy savings	17

BFM 3.4 Shared Savings Program for Government Agencies			20

BFM 3.5 Load Management								21

BFM 3.6 Green Campus Initiatives							22

BFM 3.7  Improved Commercial Energy Codes					23

BFM 3.8 HVAC Efficiency								24

BFM 3.9 Procurement Preference							25

Industrial

BFM 4.1 Financial Incentives for Industrial EE					26

BFM 4.2 Participate in Voluntary Industry-Government and/or Industry Partnerships	29

BFM 4.3 Leak Reduction Programs							31

BFM 4.4  Substitution of High GWP Gases						32

BFM 4.5 Industrial ecology/by-product synergy					34

BFM 4.6 Negotiated Agreements							35

BFM 4.7  Encourage Combined Heat and Power					36

BFM 4.8 Specify ASTM specification C150 for portland cement			38

Comprehensive

BFM 5.1  Government Agency Requirement and Goals				39

BFM 5.2  Increase Public Benefit Fund						40

BFM 5.3  Educate residents/public/children					42

BFM 5.4  Incentives for Green Power Purchase					43

BFM 5.5  Natural Gas and Oil Conservation Fund					43

| Measure: | BFM 1.1 Energy Efficiency Appliance Standards |
| --- | --- |

# Sector:			Residential, Commercial

Policy Description:	For appliances not covered under federal standards, the state can set minimum levels of efficiency for specific appliances.

# BAU Policy/Program:	Legislation proposed, never passed.  LED kits for traffic signals have been purchased to address traffic lights in Maine.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Set minimum efficiency standards for the following products:

| Product | Unit Sales in ME (Number of Units) | Savings in 2010 (GWh or BBtu) | Savings in 2020 (GWH or BBtu) | Unit Savings (kWh or therm) | Lifetime (years) | Incremental Cost * ($) |
| --- | --- | --- | --- | --- | --- | --- |
| Dry type transformers |  | 6.9 | 19.3 | 16.6kWh/kva | 30 | 3/kva |
| Commercial refrigerators & freezers |  | 1.2 | 2 | 430 | 9 | 29 |
| Exit signs |  | 3.7 | 10.3 | 223 | 25 | 20 |
| Traffic signals |  | 1.7 | 3.1 | 431 | 10 | 85 |
| Torchiere lamps |  | 66.9 | 121.7 | 288 | 10 | 15 |
| Set-Top boxes |  | 96.7 | 96.7 |  | 5 |  |
| Unit heaters (therm savings) |  | 63.8 | 179.7 | 268 | 19 | 276 |
| Commercial Clothes Washers |  | 1.2 | 1.8 | 197 | 8 | 200 |

Source: ENE, Communication with M Stoddard; NEEP, 2003.  The original numbers from this table are in the NEEP report “Energy Efficiency Standards: A Low Cost, High Leverage Policy for Northeast States.  Appendix A of the report cites sources for the numbers.

* Note: Incremental costs are difficult to calculate because there is almost always a range of products with varying prices.

# All of these appliances can be regulated by the state, and do not require a federal waiver.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | <0.01 | <0.01 |
| Indirect Emission Reductions (‘000 MTCO2)* | 48.4 | 68.4 |
| Total Emission Reductions (‘000 MTCO2) | 48.4 | 68.4 |
| Cost Effectiveness ($/MTCO2) |  | -239 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

Indirect Emissions are based on a projection of the average NEPOOL emission factor.

Need to update savings estimates based on changes to table above; will differ from NEEP analysis because the electricity emission factor is different.

| Measure: | BFM 2.1 Improved Residential Building Energy Codes |
| --- | --- |

# Sector:	Residential

Policy Description:	Require buildings to meet the most recent energy code efficiency/performance standards established by the International Code Council.  Continually adopt new energy codes as they are developed.

BAU Policy/Program:	Residential: State-developed code, less stringent than 1992 MEC, mandatory statewide; Voluntary IECC 2000

Maine has held four meetings of the Building Code Working Group starting in March 2003. The purpose of this group is to 1.) Survey stakeholders and determine where they stand on the issues 2.) Determine which code, NFPA or ICC, to adopt 3.) Make recommendations on how the chosen code is going to be implemented and enforced. (Source: www.bcap-energy.org)

DPUC Working Group also.

On 3/17, the committee asked the PUC to do a study and report back next session.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

- Residential building energy codes are updated every 3 years and adopted by ME 18 months thereafter.

# Each building energy code revision achieves the same percentage of savings.

# Includes BFM 2.2 Training and Enforcement of Building Energy Codes

| Data Need | Assumption | Source |
| --- | --- | --- |
| Energy Savings |  |  |
| Fossil Fuel savings per home (IECC 2000 compared to current construction in ME) | 10% | David Weitz, Building Code Assistance Project for Maine PUC public hearing on Nov 25th 2003 |
| # of new residential buildings built each year | 6,760 single family homes | Maine-specific data from National Association of Home Builders |
| # of residential buildings that comply with new codes | 70% | Estimated |
| Costs |  |  |
| New residential energy codes | NA |  |
| Increased cost for enforcement | $150,000 | Estimate |
| Increased cost for training | $200,000 | Based on programs in Texas and New Hampshire that provide training on residential codes and produce and distribute video recordings |

# NA:  Data not available at this time

Potential Barriers/Issues:  Avoid conflict with building rehab code

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 17.8 | 46 |
| Indirect Emission Reductions (‘000 MTCO2)* | 0.3 | 0.8 |
| Total Emission Reductions (‘000 MTCO2) | 18.1 | 46.9 |
| Cost Effectiveness ($/MTCO2) |  | -46 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 2.2 Training and Enforcement of Building Energy Codes |
| --- | --- |

# Sector:	Residential, Commercial

Policy Description:	Building codes are not effective unless implemented.  Train builders, code officials, architects, etc. on building codes

BAU Policy/Program:	Maine DPUC has joined with NEEP’s “Northeast Regional Building Energy Codes Project” to enforce building codes.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Included under BFM 2.1 Improve Residential Building Energy Codes, and BFM 3.7 Improve Commercial Building Energy Codes

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) |  |  |
| Indirect Emission Reductions (‘000 MTCO2)* |  |  |
| Total Emission Reductions (‘000 MTCO2) |  |  |
| Cost Effectiveness ($/MTCO2) |  |  |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 2.3 Voluntary Green Building Design Standards |
| --- | --- |

# Sector:	Residential

Policy Description:	Create voluntary high efficiency and sustainable building standards that builders can follow (e.g., Energy Star and LEED building standard).  In addition to an energy efficiency requirement, require procurement standard for concrete containing up to 20% recovered mineral component.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| # of new homes built in ME | 6,760 single family homes | Maine-specific data from National Association of Home Builders |
| # of new homes meeting higher standard | 10% per year | Estimated |
| Savings between Energy Star and standard construction (based on 1992 Code Standards) | 30% | EPA |
| Incremental Cost between Energy Star and standard construction (based on 1993 MEC) | $2150/home | EPA. Note: Price varies depending on house size, prevailing construction practices, availability of equipment, etc. For example, an Energy Star labeled home can actually be less expensive to build than its non-Energy Star counterpart (i.e., good insulation, high performance windows, etc. can lower the heating and cooling loads so much that smaller and less expensive HVAC equipment and more compact duct runs are able to be installed, saving significant first costs.) |
| Residential Concrete Consumption | 380,000 to 400,000 cubic yards in 2003 | PCA Portland Cement and Construction Forecast for Maine. |
| Incremental Cost between concrete and slab | 0 | Dragon Products - Slag is comparable in cost to cement |

# Owning (i.e., mortgage amortization) and operating (i.e., utility bills) an Energy Star labeled home costs less than owning and operating a non-Energy Star labeled home.  This is because we do not recommend energy-saving measures unless the amortized cost of implementing those measures is less than the utility bill savings resulting from them.  Source:  EPA Energy Star Homes

# GHG emission savings are estimated assuming BFM 2.1 is not implemented. If implemented, GHG emission savings will be decreased.

# Note: This option may potentially be funded through BFM 5.2

- A procurement standard for concrete containing a minimum of 20% slag would result in a CO2 savings of over 20,000 short tons per year of direct and indirect emissions (18,144 metric tons).

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 7.8 | 14.2 |
| Indirect Emission Reductions (‘000 MTCO2)* | 2.4 | 4.4 |
| Total Emission Reductions (‘000 MTCO2) | 10.2 | 18.6 |
| Cost Effectiveness ($/MTCO2) |  | -64 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emission reductions at the site of electricity generation

Indirect Emissions are based on a projection of the average NEPOOL emission factor.

Note:  Emission reductions from a procurement standard for concrete are not yet included in the table.  Need to double check that they are not already accounted for in BFM 4.8.

| Measure: | BFM 2.4 Energy Efficiency/Location Efficient Mortgages |
| --- | --- |

# Sector:	Residential

Policy Description:	1) Recommend that the PUC's Efficiency Maine Program take steps to promote Energy Efficient Mortgages (EEMs) to Maine home buyers and homeowners that qualify. An EEM is a mortgage where the cost of installing “cost effective” energy improvements can be included in the total amount being financed (or refinanced) in any HUD/FHA, VA, or Fannie Mae mortgage. Homebuyers can generally finance from $3,000 to $8,000 worth of energy improvements directly into their mortgage so long as a Home Energy Rating System (HERS) Provider documents that the expected average monthly energy savings will be greater than the small amount added to the monthly mortgage payment to cover the $3,000 to $8,000 EEM. In Maine and New Hampshire, almost every home can gain significant energy savings from just a few hundred to a few thousand dollars worth of “targeted” energy improvements (http://www.horizon-res.com/EEMs.htm).

2) Support the recommendation of the housing roundtable to make Location-Efficient Mortgages SM (LEM) available in Maine. From a roundtable discussion on housing issues for Maine's Congressional Delegation to consider, Portland, August 5, 2003:  Expand the availability of the Location Efficient Mortgage SM  (LEM). Now offered by Fannie Mae only in Seattle, San Francisco, Los Angeles, and Chicago, LEMs increase the borrowing power of homebuyers by up to 30% by taking into account the money they save by living in urban neighborhoods where they can walk, bicycle, or use public transit. In Southern Maine, LEMs would enable young families earning 80% of median to qualify for homes in Portland, South Portland, and Westbrook, which range from $170,000-$190,000, instead of lower priced homes in rural areas, such as Gray or Hollis, which range from $144,000-$160,000. (http://216.239.37.104/search?q=cache:MWd75fm6TrIJ:www.nhc.org/yrendrtb03portlandme.pdf+Location+Efficient+Mortgage+%2B+Maine&hl=en&ie=UTF-8)

BAU Policy/Program:	EEMs are available in Maine, but it is likely that they are not yet widely understood, marketed, or sold.  Location Efficient Mortgages are not currently offered in Maine. Location Efficient Mortgage services are available in the cities of Chicago and Seattle; Los Angeles County; and the nine-county San Francisco Bay Area. The mortgage services are currently part of an underwriting experiment sponsored by Fannie Mae.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Energy Efficiency Mortgages |  |  |
| Average annual energy savings per home |  |  |
| Electricity | 3% | Energy Rated Homes of Vermont |
| Fossil Fuel | 39% | Energy Rated Homes of Vermont |
| # of homes resold each year in ME | 13,246 | Maine Real Estate Information System (MREIS) |
| # of home buyers participating in Mortgage Program | 1% | Estimate |
| Cost of implementing program | $2353/home | Fannie Mae: Placeholder data |

# NA: Data not currently available.

Calculating Savings for Location Efficient Mortgages:  By drawing on land-use information such as population density and public transit locations, and census information on car ownership and driving levels, a lender can predict how much a household in a particular location will spend on transportation. Based on this prediction, the lender calculates the difference in transportation costs between an urban household and its suburban counterpart. This dollar amount is then added onto the buyer's qualifying income. The amount can be substantial, as it takes into account savings on vehicle purchases and maintenance, auto insurance, and fuel (the formula for calculating these savings was developed specifically for the Location Efficient Mortgage® program). (Source: NRDC)  Note Coordinate with Transportation Working Group to develop GHG estimates and costs.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 2.0 | 4.9 |
| Indirect Emission Reductions (‘000 MTCO2)* | 0.1 | 0.2 |
| Total Emission Reductions (‘000 MTCO2) | 2.0 | 5.1 |
| Cost Effectiveness ($/MTCO2) |  | -19 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 2.5 Education to homeowners |
| --- | --- |

# Sector:	Residential

Policy Description:	Educate homeowners on EE and sustainable design retrofits, renovations and new construction options (e.g., provide EE education materials at time of resale or refinancing).

BAU Policy/Program:	Education programs under Efficiency Maine; Programs by DEP

There are two energy education programs operating in Maine. One program, the Maine Energy Education Program (MEEP), provides education on energy is-sues to kindergarten through twelfth grade students in the Bangor Hydro-Electric and Central Maine Power service territories. A second program, operated by Maine Public Service Company, offers educational pro-grams in the Maine Public Service territory. Both programs strive to increase consumer knowledge of energy efficiency - a fundamental market barrier to economically efficient behavior. (Anticipated budget 2004: $417,560)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# What type of program is envisioned?

# When/Where/How would homeowners be targeted?

# During building inspection at time of resale

# Mandatory efficiency ratings on furnaces/boilers/other equipment

# Through electricity billing

# Pass on to Education Working Group

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 2.6 Efficient Use of Oil and Gas: Home Heating |
| --- | --- |

# Sector:	Residential

Policy Description:	Provide incentives for EE retrofits or upgrades for home heating equipment, hot water heaters, programmable thermostats

BAU Policy/Program:	LIHEAP, WAP, REACH Central Heating Improvement (CHIP) Programs for low-income residents. (Energy Advisors, LLC, 2003)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Sources |
| --- | --- | --- |
| Oil Furnaces/Boilers |  |  |
| # operating at or below 60% AFUE | 15% | Expert judgement |
| Energy savings associated with replacing 60% AFUE furnace with Energy Star oil Furnace (90% AFUE) | 24.25 MMBTU/furnace | Calculated based on 20% efficiency increase and avg 80.8 MMBTU/household for space heating |
| Estimated cost of conventional oil furnace | $2000 | EPA |
| Estimated cost of Energy Star oil furnace | $2700 | Consumer Energy Council of America (2001) |
| Market penetration | 2% | Estimated |
| Natural Gas Furnaces |  |  |
| # operating at or below 60% AFUE | 15% | Expert Judgement |
| Energy savings associated with replacing 60% AFUE furnace with Energy Star natural gas furnace (90% AFUE) | 25.25 MMBTU/furnace | Calculated based on 20% efficiency increase and avg 80.8 MMBTU/household for space heating |
| Estimated cost of conventional natural gas furnace | $2000 | EPA Energy Star |
| Estimated cost of Energy Star natural gas furnace | $2500 | EPA Energy Star |
| Market Penetration | 2% | Estimated |
| Integrated hot water heater |  |  |
| Average energy factor of stand alone water heater more than 10 years old | 50% | USDOE Building Technologies Program |
| Energy factor of new integrated hot water heater | 88% | USDOE Building Technologies Program |
| Cost of installation | 900 | USDOE Building Technologies Program |
| Market Penetration | 2% of oil heated homes; 2% natural gas heated homes | Assume install with furnace replacement |
| Set-back Thermostat |  |  |
| Energy Savings per year | 5% | EPA (Ranges from 5 to 30%)- Energy Star requires 2 programs with 4 settings each |
| Cost | $195 | EPA (product cost ranges from 40-120; installation charge of 25-75) |
| Market Penetration | 2% of oil heated homes; 2% natural gas heated homes | Assume install Energy Star Programmable Thermostat with boiler replacement |
| Percentage of Homes by Heating Fuel Type |  |  |
| Oil | 80% | US Census, 2000 |
| Natural Gas | 8% | US Census, 2000 |
| Electricity | 4% | US Census, 2000 |
| Number of homes in ME | 518,200 | US Census, 2000 |

- Note: This option may potentially be funded through BFM 5.2

- Further information to be provided from MODA via John Batey, P.E.

- Subgroup (Pattie Aho, Jamie Py, Michael Stoddard, Brian Hubbell) considering measure

Maine Oil Dealers Recommended Improvements to Oil Heat Systems

| Recommended Improvment | Estimated Savings |
| --- | --- |
| Heating System Tune | 2 to 10% |
| Reduced firing rate or nozzle reduction | 6 to 10% |
| Reduced temperature of circulating water/furnace air | 5 to 12 % |
| Pipe and duct insulation | 5 to 10% |
| Flame retention head burner | 15 to 20% |
| New high-efficiency hot water boiler | 20 to 40% |
| New high-efficiency warm air furnace | 20 to 40% |

Source: Maine Oil Dealers web site- www.meoil.com

.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 26.1 | 34.7 |
| Indirect Emission Reductions (‘000 MTCO2)* | 0.0 | 0.0 |
| Total Emission Reductions (‘000 MTCO2) | 26.1 | 34.7 |
| Cost Effectiveness ($/MTCO2) |  | 4 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.1 Energy standards for New Construction/Renovations |
| --- | --- |

## Sector:	Commercial

Policy Description:	New construction as well as major renovations of all building projects that receive some state funding (state facilities, local schools, etc.) are required to be at least 20% more efficient than required by the then current state energy codes.

BAU Policy/Program:	The State of Maine has recently passed two pieces of legislation regarding this issue:  1) The Development of optimal energy efficiency in state state-funded construction (requires buildings be designed and built to standards of energy efficiency that are always at least 20% higher than the minimum energy standard s required by the then current state energy codes), and 2) Construction of schools (amends rules on construction of new schools to require that all construction proposals must be based on the most energy and environmentally efficient designs per the statute).

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumptions | Sources |
| --- | --- | --- |
| Total sq ft of state-funded buildings built each year | 204,750 | Maine Bureau of General Services |
| Total sq ft of state-funded buildings renovated | 131,250 | Maine Bureau of General Services |
| Total sq ft of schools built each year | 384,750 | Maine Bureau of General Services |
| Requirement by State of Maine for energy savings compared to minimum energy standards required by current state energy codes | 20% | Maine EO |
| Incremental cost | $4/sq ft | Katz et al. (2003) |

NA: Data not available

D Baston thinks incremental cost should be more like $2/sq foot; waiting for study (NJ study of 20% of ASHRAE)

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 1.8 | 4.8 |
| Indirect Emission Reductions (‘000 MTCO2)* | 3.0 | 8.0 |
| Total Emission Reductions (‘000 MTCO2) | 4.9 | 12.8 |
| Cost Effectiveness ($/MTCO2) |  | 47 |

| Measure: | BFM 3.2 Incentive Payment for Energy Efficient Buildings |
| --- | --- |

## Sector:	Commercial

# Policy Description:	Encourage privately financed new construction and renovation to be high performance buildings by certifying to 20% above existing code.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Number of commercial buildings built each year | 2,184 | CT data scaled to ME. Placeholder- Waiting for data from Central Maine Power |
| Market penetration | 2% | Estimate |
| Energy Savings compared with then current code | 20% | As per recommendation |
| Average energy intensity for non-governmental buildings |  |  |
| Electricity | 13.4 kWh/sq ft | EIA CBECS (1999) |
| Natural Gas | 43.1 cu ft/sq ft | EIA CBECS (1999) |
| Oil | 0.18 gallons/sq ft | EIA CBECS (1999) |
| Incremental Cost | $4/sq ft | Katz et al. (2003) |

Note:  This option may potentially be funded through BFM 5.2

D Baston thinks incremental cost should be more like $2/sq foot; waiting for study (NJ study of 20% of ASHRAE)

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 1.4 | 3.7 |
| Indirect Emission Reductions (‘000 MTCO2)* | 2.0 | 7.5 |
| Total Emission Reductions (‘000 MTCO2) | 4.3 | 11.3 |
| Cost Effectiveness ($/MTCO2) |  | 29 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.3 Encourage state to fund fastest most cost-effective energy savings |
| --- | --- |

# Sector:	Commercial/Government Agency Buildings

Policy Description:	D Bergeron working on language for recommendation.  A program to encourage measurement and tracking of energy consumption, strategic planning, and benchmarking against other buildings.

BAU Policy/Program:	 25% energy reduction goal by 2010 (relative to 1998 baseline) added to Energy Conservation Building Act for Public Buildings. This legislation established a pilot program to seek to achieve that level of energy savings in ten facilities of over 40,000 square feet. Under the pilot program, energy savings are to be achieved through performance contracts with energy service companies.

LD845 Climate Change:  This bill requires new sources of greenhouse gases to be reported to the Department of Environmental Protection.  It also requires the department to create an inventory of greenhouse gas emissions associated with state-owned facilities and state-funded programs and to create a plan for reducing those emissions.

The Maine Public Utilities Commission and the Maine Department of Administrative and Financial Services

(DAFS) developed a Memorandum of Understanding (MOU) to improve the energy efficiency of State buildings. The program will fund renovations that enhance electrical efficiency. It will also fund an energy survey of all state buildings to identify opportunities for energy efficiency. Under the MOU, DAFS identifies potential projects and Efficiency Maine reviews the proposed projects for cost effectiveness. If the projects are

cost effective, they are developed and managed by DAFS and financed through mechanism through Maine PUC to DAS.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

Following table was moved from BFM 3.4 :

| Data Needs | Assumption | Source |
| --- | --- | --- |
| State Agency Fuel Consumption |  |  |
| Electricity | 127,384 MWh | Energy Advisors, LLC |
| Natural Gas | 90,025 MMBTU | Estimated using government to commercial sector electricity share |
| Oil | 643,062 MMBTU | Estimated using government to commercial sector electricity share |
| Government building share of commercial sector electricity consumption | 3% | Energy Advisors, LLC |
| Reduction in state energy use by 2010 | 25% | Section 1770 |
| Reduction in state energy use by 2020 | 50% | Estimated |
| Costs | $0.3/kWh | Placeholder: based on Maine Efficiency results from State Building Program |

NA: Data not available

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 13 | 28.5 |
| Indirect Emission Reductions (‘000 MTCO2)* | 8.6 | 18.8 |
| Total Emission Reductions (‘000 MTCO2) | 21.6 | 47.3 |
| Cost Effectiveness ($/MTCO2) |  | -108 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.4 Shared Savings Program for Government Agencies |
| --- | --- |

# Sector:	Commercial/Government Agency Buildings

Policy Description:	Incentive program for state agencies achieving savings through energy conservation, with portion of savings retained by agency for future energy costs/activities. (Captured under BFM 3.3- WG felt this measure should come off the table)

BAU Policy/Program:	Under a law passed in 1991, the Bureau of Public Improvements (predecessor to the Bureau of General Services) was charged with developing a program “in which an eligible department or agency of the State may retain a portion of any first-year energy cost savings demonstrably attributable to energy efficiency improvements undertaken by that department or agency.”105 The Bureau was required to submit the proposed program to the legislative Committee on State and Local Government by January 1, 1992. It does not appear that this program was ever implemented. (Energy Advisors, LLC, 2003)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

See BFM 3.3

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.5 Load Management |
| --- | --- |

# Sector:	Commercial

# Policy Description:	Overcome existing regulatory barriers to increase the market diffusion of third party load management for non-intrusive commercial loads (e.g., dimming lights, planned cycling of refrigeration compressors)  Tony Buxton working on language

## BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Market Size | 1250 MW | Scaled CT market size to ME based on share of commercial electricity consumption |
| Market Penetration per year | 5% | Estimated |
| Incremental Cost | $500/kW | NXEGEN: Placeholder-BFM WG thought estimate was way too high |

NA: Data not available at this time

Central Maine Power and NE ISO have been contacted for data; Hanaford and Shaws may also be able to provide data on internal savings.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 0.0 | 0.0 |
| Indirect Emission Reductions (‘000 MTCO2)* | 2.9 | 4.7 |
| Total Emission Reductions (‘000 MTCO2) | 2.9 | 4.7 |
| Cost Effectiveness ($/MTCO2) |  | -220 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.6 Green Campus Initiatives |
| --- | --- |

Sector:	Commercial

Policy Description:  	Promote a “Green Campus” Initiative with all Maine Colleges, Universities, Private/Secondary Schools with Campus to minimize environmental impact  Dudley Greeley will elaborate

# BAU Policy/Program:  	Currently underway (USM, Others)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Duration of Proposed Program | 5 years | Estimated |
| Market Size | 27 colleges and universities with 52,441 student enrollment | Department of Education |
| Average $/student for energy | $265/Student | Based on University of Southern Maine |
| % of Market enrolled in program each year | 5% | Estimated |
| Average electricity savings | 15% | Communication with Clean Air-Cool Planet |
| Average fossil fuel reductions | 20% | Communication with Clean Air-Cool Planet |
| Cost | $0.3/kWh | Place holder based on Efficiency Maine State Building Program |

Note: This option may potentially be funded through BFM 5.2

Dudley Greeley sent out an email to the 11 colleges participating in the GCC to get numbers on energy consumption and/or savings at the colleges; no information yet.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 6.5 | 20.6 |
| Indirect Emission Reductions (‘000 MTCO2)* | 1.6 | 4.9 |
| Total Emission Reductions (‘000 MTCO2) | 8.1 | 25.5 |
| Cost Effectiveness ($/MTCO2) |  | -224 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.7 Improved Commercial Energy Codes |
| --- | --- |

# Sector:	Commercial

Policy Description:	Require buildings to meet the most recent energy code efficiency/performance standards established by the International Code Council.

BAU Policy/Program:	Commercial: ASHRAE/IESNA 90.1-2001, mandatory statewide; can COM check -EZ to show compliance (Most up to date).  Automatic adoption of commercial building energy codes.

Bill being held DPUC-7

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Included in baseline as legislation requires automatic upgrade of ASHRAE Standards.

| Data Need | Assumption | Source |
| --- | --- | --- |
| Annual Commercial Savings |  |  |
| Oil savings | NA |  |
| Natural gas savings | NA |  |
| Electricity savings | NA |  |
| New commercial buildings built each year | 2,184 | CT data scaled to ME |
| Number of commercial buildings that comply with new codes | 70% | Estimated |
| Costs |  |  |
| Cost for new commercial building code | NA |  |
| Cost for enforcement | NA |  |
| Cost for training | NA |  |

# NA:  Data not available at this time

Potential Barriers/Issues:  Avoid conflict with Rehab code

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.8 HVAC Efficiency |
| --- | --- |

Sector:	Commercial

Policy Description:  	 Retrofit existing HVAC systems with most current energy efficient technology. T Buxton and D Bergeron to work on policy description

# BAU Policy/Program:  	 Efficiency Maine C&I Program, available to businesses with > 50 FTEs, includes three components (1) business practices training, (2) information and end-use training opportunities, and (3) financial grants to assist in the purchase of EE equipment.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Savings associated with installing HVAC computer technology (based on adaptative/fuzzy logic control) | 5% | DOE Buildings Technology Program |
| Commercial Building Energy Used for HVAC as percentage of primary energy use | 30% | DOE Buildings Technology Program |
| Market penetration | NA |  |
| Costs associated with installing computer technology | NA |  |

NA: Data not available

Optimal Energy Study for Public Advocate looks at electrical energy savings potentail and cost for the following commercial sector measures:

Efficient Lighting

Efficient Air Conditioning

Building System Controls

Enhanced Envelope Measures

Efficient Appliances

High Efficiency Motors

Variable Frequency Drives

High Efficiency Refrigerators

Exeter study for Public Advocate estimates Technical potential for Commercial measures (listed above) between 2003 and 2012 is 2,201,337 MWh for small businesses and 2,801793 MWh for non-small businesses.

NASEO (Estimating Energy and Cost Savings and Emission Reductions for the State Energy Program Based on Enumeration Indicators Data) estimated 20% savings for HVAC retrofits.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 3.9 Procurement Preference |
| --- | --- |

# Sector:	Buildings Facilities and Manufacturing

Policy Description:	Specify procurement preference for concrete and concrete products that contain a recycled mineral component (specifically ground granulated blast furnace slag [slag]) of a minimum of 20% for publicly funded projects

BAU Policy/Program:	ASTM specifies standards for the inclusion of slag to concrete.  MDOT specifications allow for the inclusion of slag in concrete.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

Slag is derived from a by-product of the steel industry.  It is processed and grounds to meet strict specifications and sold as a cementitious (cement-like) product.  Slag has cementitious properties and can be used to offset a portion of the cement used in concrete mixtures.  How much can be offset is dependent on season (winter/summer), set requirements and other factors.

- 550 lbs cement is used per yard of concrete (average)

- Approximately, 880,000 cubic yards of concrete for all applications in Maine in 2003.  (based on data from USGS for Cement consumption)

- Approximately 315,000  to 350,000 cubic yards of concrete used for public buildings, structures, and transportation.

- Use of 20% slag as a replacement for cement yields savings of approximately 18,000  to 20,000 tons of CO2 per year.

- This is a conservative estimate based on slag.  Use of other recycled mineral components such as fly ash or silica fume may be different.  Slag usage may be higher (30 to 40%) and result in higher CO2 savings.

Concrete consumption includes commercial, residential, industrial  and government consumption.  Transportation accounts for approximately 215,650 cubic yards (PCA Construction Forecast, February 2004).  Approximately 22,000 tons of slag were used in concrete in 2003 for all uses.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

Potential Barriers/Issues:  Slag is comparable in cost to cement.  Availability may be limited.  May require a capital investment of additional silo storage for some suppliers.

| Measure: | BFM 4.1 Financial Incentives for Industrial EE |
| --- | --- |

# Sector:	Industrial

Policy Description:	Offer financial incentive/rebates for EE improvements taken at ME industries  Subgroup working on this measure (T Buxton, M Stoddard, C Kraske)

# BAU Policy/Program:	Efficiency Maine has established a new Commercial and Industrial Program for Maine businesses that provides a combination of services, including energy efficiency information and training, business practice assistance, and direct financial incentives in the form of grants. The components of the program are designed to encourage businesses to adopt energy efficient business practices, to include consideration of energy costs and energy efficiency in their business decisions, and to purchase and install energy efficient products.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Performance of Efficiency Maine’s C&I program | 10 kWh/$ | CT’s Energy Opportunities program; up to 30% cost share- Placeholder- Central Maine Power may have numbers here |
| Level of increased funding | $2 million | Estimate |

# Note: This option may potentially be funded through BFM 5.2

Optimal Energy Study for Public Advocate looks at electrical energy savings potential and cost for the following industrial sector measures:

Efficient Lighting

Efficient Ventilation and Cooling

Efficient Process Controls

Building System Controls

Variable Frequency Drives

High Efficiency Air Compressors

Exeter study for Public Advocate estimates Technical potential for Industrial measures (listed above) between 2003 and 2012 is 3,341,338 MWh

# Many states have provided financial incentives for energy savings in the private sector. Efficiency incentives primarily appear in one of three forms- grants, loans and tax incentives.

| Financial Incentive | Example |
| --- | --- |
| Corporate tax incentives | The Maryland Clean Energy Incentive Act provides Maryland sales tax exemptions or income tax credits when purchasing certain qualifying high efficiency Energy Star appliances, electric and hybrid-electric vehicles, and certain renewable resource energy systems. The Act also provides for a personal or corporate income tax credit for the production of electricity from commercial and industrial waste, forestry (excluding old growth residue) and agricultural by-products, and landfill and anaerobic digestion biogas. The credit is 0.85¢/kWh (or 0.5¢/kWh for electricity generated in a co-fired plant). The electricity must be sold to an unrelated party to take advantage of the credit. The unused amount of the credit may be carried forward and applied for succeeding taxable years for up to ten years. (Website: http://www.energy.state.md.us/programs/cleanincentives.html ) |
| Property Tax Reduction | Montana generating plants producing 1 megawatt or more by means of an alternative renewable energy source are eligible for the new or expanded industry property tax reduction on the local mill levy during the first nine years of operation, subject to approval by the local government. If so approved, the facility is taxed at 50 percent of its taxable value in the first five years after the construction permit is issued. Each year thereafter, the percentage is increased by equal percentages until the full taxable value is attained in the tenth year. (Website: http://www.deq.state.mt.us/energy/Renewable/TaxIncentRenew.asp#15-24-1401) |
| Business Energy Tax Credit | Oregon Department of Energy: Tax credit to those who invest in energy conservation, recycling, renewable energy resources and less-polluting transportation fuels. The tax credit is 35 percent of the eligible project costs - the incremental cost of the system or equipment that's beyond standard practice. You take the credit over five years: 10 percent in the first and second years and 5 percent each year thereafter. If you can't take the full tax credit each year, you can carry the unused credit forward up to eight years. Those with eligible project costs of $20,000 or less may take the tax credit in one year. http://www.energy.state.or.us/bus/tax/taxcdt.htm |
| Cash Incentives | In cooperation with Narragansett Electric Small Business Program, The Rhode Island State Energy Office, (RISEO) is providing cash incentives to small commercial/industrial applicants (<100KW per month) who install high-efficiency heating equipment measures (e.g., temperature control, EMS, steam trap replacement, boiler reset controls, etc.). All incentives capped at 25% of installed cost or $3,000 per building, whichever is lower. Oregon’s Industrial Energy Savings Plan (ESP) offers cash incentives for industrial facilities and manufacturing processes to improve their energy efficiency. Typical opportunities include building and process controls, adjustable frequency drives, compressed air systems, exhaust systems, material handling systems, fans and pumps, lighting, and process efficiency improvements. Incentives are based on the measured reduction in energy use resulting from installing energy-efficient equipment instead of standard equipment in new installations. Incentives are paid following project completion, commissioning and verification of energy savings. (Source: EWEB) Entergy’s Large C&I program offers incentives for demand savings and/or energy savings. The incentive prices may not exceed 35% of the avoided costs of supplying electricity (e.g., $164/kW or $0.056/kWh). |
| Zero/Low Interest Loan Program | Indiana’s Industrial Energy Efficiency Fund is a zero-interest loan program geared to help manufacturers increase the EE of their manufacturing process. The fund is used to replace or convert existing equipment, or to purchase new equipment as part of a process/plant expansion, which will lower energy use. Companies can receive as much as $250,000. (Potential in Maine under FAME?) Zero interest loans are not successful. Private companies don’t like putting borrowing on the balance sheet |
| Rebates | EWEB Energy-Efficient Motor Program offers rebates to EWEB's commercial and industrial customers for purchasing energy- efficient, three-phase electric motors between three horsepower and 500 horsepower. To be eligible, motors must be meet minimum nominal full load efficiencies published by EWEB and must be installed or inventoried within EWEB's service territory. The rebate is available either from participating motor suppliers as a discount on the motor sales price at the time of purchase or from EWEB as a cash payment after the motor is purchased. |
| Bonds | Bonds provide up-front capital by attracting investment in the credit-worthiness of an institution |

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.2 Participate in Voluntary Industry-Government and/or Industry Partnerships |
| --- | --- |

## Sector:	Commercial, Industrial

Policy Description:	Recognize voluntary programs and reward actions in the appropriate sectors. While some programs already exist at the national level, there may also be an opportunity to develop additional programs in Maine.

BAU Policy/Program:   	Several programs already exist at the national level:  EPA Climate Leaders, DOE Industries of the Future (Maine Industries of the Future currently includes pulp and paper, secondary wood, and metals industry), EPA Energy Star Benchmarking Program, DOE Rebuild America; Maine STEP-UP program, Carbon Challenge, Climate Vision

Clean Air-Cool Planet program highlights include MOU’s with Star supermarket, Timberland company, Tom’s of Maine, Oakhurst Dairy, Poland Spring, York hospital

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# DOEs suggestions for expanding Maine participation in IOF:

# Include agriculture and plastics and potentially welding

# Additional publicity

# The Maine legislature might consider creating a mini state grant program that could provide funds to Maine businesses for feasibility studies to determine whether to adopt new energy-efficient technologies.

# Discuss energy and EE technologies as part of technology cluster project

# The Maine Smart Tracks for Exceptional Performers and Upward Performers, or STEP-UP, Program offers recognition and other incentives to businesses interested in implementing sustainable practices.

# Alan Auto (Portland), Bath Iron Works (Bath), Fairchild Semiconductor (South Portland), Interface Fabrics Group (Guilford), Moss, Inc. (Belfast), NorDx (Scarborough) and Poland Springs Bottling Company (Hollis). College of the Atlantic (Bar Harbor), CYRO Industries (Sanford), National Semiconductor of Maine (South Portland) and Naturally Potatoes (Mars Hill).

# Looking into whether any of the voluntary programs have been quantified

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.3 Leak Reduction Programs |
| --- | --- |

# Sector:	Industrial

Policy Description:	Reduce methane leaks from natural gas systems, reduce HFC leaks from refrigeration, motor vehicle air conditioning, etc.

BAU Policy/Program:   	Existing federal programs to reduce methane leaks from natural gas pipelines, SF6 from electricity substations

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Needs | Assumption | Source |
| --- | --- | --- |
| Increased participation in EPA Natural Gas Star | NA |  |
| Increased participation in SF6 Electrical Utility | NA |  |
| ODS substitute emissions from refrigeration and A/C | 67% | US EPA based on national statistics |
| HFC emissions from stationary refrigeration | 40% | USEPA based on national statistics |
| Market penetration | 5% per year | Estimated |
| HFC leak reduction potential for stationary refrigerants | 5% | US EPA |

# NA: Data not available at this time

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 1.2 | 9.0 |
| Indirect Emission Reductions (‘000 MTCO2)* | N/A | N/A |
| Total Emission Reductions (‘000 MTCO2) | 1.2 | 9.0 |
| Cost Effectiveness ($/MTCO2) |  | 0.27 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.4 Substitution of High GWP Gases |
| --- | --- |

# Sector:	Industrial

Policy Description:	 Substituting other gases for high GWP gases is a viable option as long as environmental, health, safety, and performance requirements can be met.

BAU Policy/Program:   	None.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Alternative Refrigerants

# Ammonia. Ammonia, primarily used in water cooled chillers, has excellent thermodynamic properties and can be used in many types of systems. However, it must be used carefully, because it is toxic and slightly flammable.  Building and fire codes restrict the use of ammonia in the urban areas of the United States and many other countries. (EPA, 2001)

# Hydrocarbons. Hydrocarbons have thermodynamic properties that make them good refrigerants; however, their high flammability causes concern for safety. Hydrocarbon refrigerant use is generally restricted by U.S. safety codes, with the exception of industrial refrigeration(EPA, 2001).

# Carbon Dioxide. Carbon dioxide has been investigated for use primarily in mobile air-conditioning systems and refrigerated transport. (EPA, 2001)

# Alternative Solvent Fluids

# In electronics, metal, and some precision cleaning end uses, alternative organic solvents with lower GWPs are being manufactured and integrated into the industry. Some of these solvents, such as HFCs, HFEs, hydrocarbons, alcohols, volatile methyl siloxanes, brominated solvents, and non-ODS chlorinated solvents, can be used as alternatives to PFC/PFPEs, CFCs, and HCFCs.

# Non-HFC Blowing Agents

# Hydrocarbons (HC) Hydrocarbons such as propane and butane are alternatives to HFCs. HCs are inexpensive and have lower GWP impacts relative to HFCs. However, key technical issues associated with hydrocarbons are: flammability, VOCx, and performance.

# Liquid Carbon Dioxide (LCD).  Foams blown with CO2 might suffer from lower thermal conductivity, lower dimensional stability, and higher density versus HCFC blown foams. To overcome these limitations, CO2 can be blended with hydrocarbons or HFCs.

# Water-Blown (in situ) Carbon Dioxide (CO2/water).  During manufacturing, no ODP or high GWP gases are emitted, and there are limited  health and safety risks during processing. However, foams produced using CO2/water are subject to the same performance limitations discussed for LCD-blown foams

# Lower-GWP HFC Substitution.  Manufactures can reduce their emissions on a carbon basis by switching from a blowing agent with a high GWP to one with a lower GWP, but any associated energy penalties must also be considered.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.5 Industrial ecology/by-product synergy |
| --- | --- |

# Sector:	Industrial

Policy Description:	Programs to link the by-products from one industry with use as the feedstock for other industries.

BAU Policy/Program:   	Beneficial use stakeholder process held in State.  Process identified barriers including liability language and classification of by-products as hazardous waste in EPA regulation

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

Ann Thayer and Chuck Kraske providing examples of potential projects that could lead to GHG savings

Potential data source: Denmark industrial park

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.6 Negotiated Agreements |
| --- | --- |

# Sector:	Industrial

Policy Description:	To promote GHG reductions in particular sectors, a state government may enter into direct voluntary or negotiated agreements with industries or industrial sectors. Negotiated agreements, for example, would result in agreed-upon GHG emission reductions or offsets as an alternative to compliance or enforcement actions resulting from violation of air pollution legislation (such as violations of Clean Air Act SIP requirements), or as an alternative for possible regulation of GHG emissions.

BAU Policy/Program:

LD845 Climate Change:  This bill requires new sources of greenhouse gases to be reported to the Department of Environmental Protection. The bill also requires the department to enter into carbon emission reduction agreements with nonprofit organizations and businesses.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Supplemental Environmental Projects (SEP); Can we work GHG component into these projects?

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 4.7 Encourage Combined Heat and Power |
| --- | --- |

# Sector:	Industrial

Policy Description:	Combined heat and power (CHP) is the simultaneous production of electricity and heat using a single fuel. The heat produced from the electricity generating process is captured and utilized to produce high and low level steam. The steam can be used as a heat source for both industrial and domestic purposes and can be used in steam turbines to generate additional electricity (combined cycle power).

BAU Policy/Program:   	CHP units are included as eligible renewable sources under the state Renewable Resource Portfolio Requirement

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

For preliminary analysis, following assumptions were made:

# EEA MW potential represents technical potential only, and does not evaluate economic potential.  EEA assumes commercial units are reciprocating engines less than 5 MW, industrial units are simple-cycle combustion turbines of 5-10 MW capacity.

# Based on EGRID data, CHP capacity factor assumed to be 0.4 for commercial, 0.6 for industrial.

# CHP electric efficiency assumed to be 0.4 for both commercial and industrial.

# Power-to-heat ratio assumed to be 0.8 for all units based on units of similar capacity in EGRID.

# All CHP units assumed to be fired by natural gas.

# Fuel input of stand-alone boilers replaced assumed to be 2/3 gas, 1/3 oil (Btu basis).  Oil is assumed to be distillate fuel.

# Efficiency of stand-alone boilers assumed to be 80%.

| Data Need | Assumption | Source |
| --- | --- | --- |
| Technical potential of CHP capacity in Maine in 2010 (MW) |  |  |
| Commercial (MW) | 411 |  |
| Industrial (MW) | 232 |  |
| Total (MW) | 643 |  |
| Technical potential of CHP capacity in Maine in 2020 (MW) |  | EEA |
| Commercial (MW) | 411 |  |
| Industrial (MW) | 232 |  |
| Total (MW) | 643 |  |
| Economic potential of CHP capacity in ME | NA |  |

NA: Data not available

# T Buxton, M Stoddard, and D Baston will do more work on economic CHP potential – focus on small industry, large commercial applications.  Potential data sources include: trade associations in DC, DOE

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) |  |  |
| Indirect Emission Reductions (‘000 MTCO2)* |  |  |
| Total Emission Reductions (‘000 MTCO2) | 365 | 355 |
| Cost Effectiveness ($/MTCO2) |  | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

# * Indirect Emissions are based on a projection of the average NEPOOL emission factor.

Measure 4.8: 		Specify ASTM specification C150 for portland cement

Sector:			Manufacturing

Policy Description:     	Specify ASTM (American Society for Testing and Materials ) specification C150 for Portland cement rather than AASHTO (American Association of State Highway Officials).

BAU Policy or Program:  MEDOT currently specifies AASHTO specifications.

ASTM is the American Society for Testing and Materials, the largest voluntary standard development system in the world.  The manufacturing of portland cement is outlined in ASTM standard C150.  ASTM C 150 was recently amended to allow for the inter-grinding of up to 5% limestone in Portland cement while maintaining all performance specifications.  The amended specification lowers the overall carbon intensity of the portland cement.   This standard is consistent with standards already in place in Mexico and Canada.   EPA supports this revised standard due to the potential for CO2 reductions.  The ASTM standards Board is currently working to harmonize the revised standard with existing AASHTO (American Association of State Highway Officials) standards, which do not recognize this amended standard.

Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates

- Approximately 450,000 tonnes of cement were produced in Maine in 2003.

- If Maine and the surrounding states adopt the ASTM standard C 150, up to 5% limestone can be introduced in the final grind of cement as long as all other performance standards are met.

- Based on experiences from Canada and European cement manufacturers, a conservative figure that 2.5% limestone addition is possible.

- This results in a reduction of approximately 10,000 tonnes of CO2. (9072 metric tonnes)

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 9 | 9 |
| Indirect Emission Reductions (‘000 MTCO2)* |  |  |
| Total Emission Reductions (‘000 MTCO2) | 9 | 9 |
| Cost Effectiveness ($/MTCO2) |  | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

# * Indirect Emissions are based on a projection of the average NEPOOL emission factor.

Potential Barrier/Issues There are no cost implications for adopting the revised standard.

| Measure: | BFM 5.1 Government Agency Requirement and Goals |
| --- | --- |

# Sector:	Comprehensive

Policy Description:	Energy efficiency (covered in Shared Savings Programs), Renewable Energy requirement/goal, procurement of environmentally sound services or products, recycling, etc.

BAU Policy/Program:   	EE goal of 25% below 1998 levels by 2010 (see above); Clean Government Initiative (DAFs, DEP) to procure EE appliances and equipment

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# What additional requirements and goals does the workgroup have in mind for gov’t agencies?  WG felt as if this measure was covered elsewhere under BFM 3.3 and 3.9.

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 5.2 Increase Public Benefit Fund |
| --- | --- |

# Sector:	Residential, Commercial, Industrial

Policy Description:	Increase surcharge on electricity and/or fossil fuel provides funding for EE measures

# BAU Policy/Program:	Efficiency Maine is funded by electricity consumers and administered by the Maine Public Utilities Commission (current funding level ~$16 million per year); no sunset date

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Electricity |  |  |
| Funds collected beyond BAU 2005-2020 | $ 15 Million | Estimated |
| 2003 Efficiency Maine Program Costs | $2,921,000 | Efficiency Maine Annual Report 2003 |
| 2003 Annual Participant Benefits | $370,150 | Efficiency Maine Annual Report 2003 |
| Savings (1st year) | 4,837 t CO2 | Efficiency Maine Annual Report 2003 |
| Lifetime of savings | 15 years | CT C&LM Fund |

# Questions WG is discussing regarding this measure

# Should this be separated out under mechanisms.

# What are we double counting? (Potentially:  BFM 2.6, 3.2, 3.3, 3.5, 3.6, 3.8, 4.1)

If we don’t include what are we missing?

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 0.0 | 0.0 |
| Indirect Emission Reductions (‘000 MTCO2)* | 81.5 | 201.7 |
| Total Emission Reductions (‘000 MTCO2) | 81.5 | 201.7 |
| Cost Effectiveness ($/MTCO2) |  | -332 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

# Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 5.3 Educate residents/public/children |
| --- | --- |

# Sector:	Residential

Policy Description:	Introduce energy efficiency and global warming into school curriculum, see measure “Education to homeowners” above.

BAU Policy/Program:	Maine Energy Education Program (MEEP) - provides funding for K-12 energy education programs; Maine energy curriculum investigation-allows task force of professional educators to develop improved energy education curriculum for use in Maine schools. (See also BFM 2.5)

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Pass on to Education Working Group

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | NE | NE |
| Indirect Emission Reductions (‘000 MTCO2)* | NE | NE |
| Total Emission Reductions (‘000 MTCO2) | NE | NE |
| Cost Effectiveness ($/MTCO2) | NE | NE |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 5.4 Incentives for Green Power Purchase |
| --- | --- |

# Sector:	Residential, Commercial, Industrial

Policy Description:	To promote and encourage the deployment of renewable energy resources in the region (beyond RPS requirements) by Maine businesses, municipalities, institutions, and households, (1) Maine ratepayers should have the choice of determining where their power comes from through a green offering(s).  (2) Government should have requirement (3) production incentive (e.g., solar hot water heater)

BAU Policy/Program:	Maine Renewable Energy is now offering on a limited basis to residential and small commercial customers in either the CMP or Bangor Hydro service territories electricity that is 100% renewable / 100% from Maine; Maine Technologies Institute coordinates Renewable Resource Fund with the State Planning Office- $70,000 for R&D at colleges, pilot program; Government lead by example- purchase 50% electricity from RE

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Sources |
| --- | --- | --- |
| Green power purchase goal in 2010 | 3% of total electricity demand | Placeholder- Contact Beth Nagusky to determine appropriate estimate |
| Green power purchase goal in 2020 | 6% of total electricity demand | Placeholder- Contact Beth Nagusky to determine appropriate estimate |
| Maine electricity demand in 2010 | 12,430,000 MWh | Maine Energy Policy Report |
| Maine electricity demand in 2020 | 13,937,000 MWh | Projection based on Maine Energy Policy Report |
| Incremental cost for RE | 0.015$/kWh | Maine Renewable Energy |

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | N/A | N/A |
| Indirect Emission Reductions (‘000 MTCO2)* | 101.4 | 224.3 |
| Total Emission Reductions (‘000 MTCO2) | 101.4 | 224.3 |
| Cost Effectiveness ($/MTCO2) |  | 56 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

* Indirect Emissions are based on a projection of the average NEPOOL emission factor.

| Measure: | BFM 5.5 Natural Gas and Oil Conservation Fund |
| --- | --- |

Policy Description:	Establish surcharge on fossil fuel to provide funding for EE measures

# BAU Policy/Program:	Complying with a federal law passed by Congress in 2000, on March 1, 2001 retail oil heat distributors in key oil heat states began assessing a fee of $0.002/gallon on all oil used to heat buildings. The funds raised from the assessment are to be used for consumer education, oil heat research and development and technical training to benefit consumers and the industry under the guidance of the National Oil heat Research Alliance (NORA).  NORA collects the fees and invests them in research projects with a large share of the funds going back to benefit the individual states. The allocation of the grant money is determined by the quality of the applications submitted and the amount of money contributed by the applicant’s home state.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Natural Gas |  |  |
| Funds collected beyond BAU 2005-2020 | $0.6 Million | Assumes 7 cents per MCF |
| Average Savings per $ for first year | 1MCF/ $29 | VT gas program- Is there a better source (D Baston); NJ about half as cost effective (DB). |
| Lifetime of savings | 15 years | CT C&LM Fund |
| Oil |  |  |
| Funds collected beyond BAU 2005-2020 | $4.5 Million | Assumes 1cent per gallon charge |
| Savings per $ | 164 barrels/$ | VT gas program- Is there a better source (D Baston) |
| Lifetime of Savings | 15 years | CT C&LM Fund |

GHG Emission and Cost Estimates:

|  | 2010 | 2020 |
| --- | --- | --- |
| Direct Emission Reductions (‘000 MTCO2) | 16.1 | 42.8 |
| Indirect Emission Reductions (‘000 MTCO2)* | 0 | 0 |
| Total Emission Reductions (‘000 MTCO2) | 16.1 | 42.8 |
| Cost Effectiveness ($/MTCO2) |  | -529 |

Direct Emissions: On-site emission reductions

Indirect Emissions: Emissions at the site of electricity generation

# Indirect Emissions are based on a projection of the average NEPOOL emission factor.

# Footnotes

Estimate appears to be conservative based on 18% reduction cited in Xenergy (2001), “Impact Analysis of the Massachusetts 1998 Energy Code Revisions”

##### The national Home Energy Ratings System (HERS) method rates a home on a scale of 0 to 100, with 0 being the least energy efficient and 100 being a highly energy efficient house. The system is based on comparing the house being rated to a computer model of that exact same house if it were built to the national Council of American Building Officials - Model Energy Code (CABO MEC) standards for residential construction. This computer modeled house is called the "Reference House." A score of 80 would be a house which meets CABO MEC standards. If the house being rated is less energy efficient than its computer modeled Reference House, then it would score less than 80 points. If the house being rated is more energy efficient than its computer modeled Reference House, then it would score more than 80 points. An EPA Energy Star® Home is a new or energy improved home which scores 86 or higher on the HERS scale. (Five Star and Five Star Plus Homes). (Source: http://www.horizon-res.com/EEMs.htm)

LOCATION EFFICIENT MORTGAGE services is a certification mark owned by the Institute for Location Efficiency. Unauthorized use of this mark is prohibited.

“Costs and Financial Benefits of Green Buildings: A Report to California’s Sustainable Building Task Force” (October 2003).  Costs based on 33 green buildings compared to conventional designs for those buildings.  The average premium was slightly less than 2% or $3-5/sq ft.

“Costs and Financial Benefits of Green Buildings: A Report to California’s Sustainable Building Task Force” (October 2003).  Costs based on 33 green buildings compared to conventional designs for those buildings.  The average premium was slightly less than 2% or $3-5/sq ft.