Maine Greenhouse Gas Action Plan Development Process

Energy Supply and Solid Waste Greenhouse Gas Reduction Options

Center for Clean Air Policy

January 28th, 2004

Contents												Page

- Overview………………………………………………………………………..2

- Criteria for Assessing and Measuring GHG Measures…………………………3

- Potential Energy Supply & Solid Waste GHG Reduction Opportunities – Edited 12-17-03………………….……………………………………………...……...4

- Preliminary GHG Savings & Cost Estimates for Priority Measures…………...9

- Energy Supply & Solid Waste Assumptions…………..……………………....10

1.  Overview

Under the direction of DEP, the Center for Clean Air Policy (CCAP) developed a set of primary and secondary criteria for assessing and prioritizing GHG measures in advance of the second Stakeholder meeting on December 17th, 2003.  The two primary criteria are the potential GHG reduction by 2020, and the cost effectiveness of these reductions.  This list of criteria can be found in Section 2 of this document.

CCAP also developed an extensive list of Greenhouse Gas Reduction options for Maine, in advance of the December 17th meeting.  Options that were popular choices in other states, or potentially high Maine GHG reduction options, or both, were denoted with a * by CCAP.  At the 12/17 meeting, the Stakeholder Advisory Group reviewed and commented on the list of options.  This Energy Supply & Solid Waste list of options can be found in Section 3 of this document.

CCAP then took this revised list of priority options, and developed preliminary GHG savings and cost estimates (see Section 4) for the priority measures identified from the 12/17 meeting.  To accompany the preliminary GHG savings and cost estimates, CCAP created a Energy Supply & Solid Waste assumptions document to identify underlying data sources and assumptions, as well areas where additional information is needed (Section 5).

2. Proposed Criteria for Assessing and Prioritizing GHG Measures

| PRIMARY CRITERIA | Indicators that would be assessed by CCAP to the extent possible using the best available data for each option. |
| --- | --- |
| GHG Impact | Total annual GHG’s reduced in relevant target years in carbon equivalents. This is typically expressed as an average annual level of projected MMTCE reduction in a given year beyond baseline emissions. GHG impacts must be quantified in order to aggregate measures toward a numerical target. |
| Cost-Effectiveness | Direct net cost divided by the GHG impact (expressed in dollars per metric ton of carbon equivalent) and is typically expressed in a given year as an average annual value over the life of the action. Costs may be expressed as a range. |
| SECONDARY CRITERIA | Indicators that would be assessed by CCAP, the Working Groups, or both when relevant for a particular option using best available data. These impacts may not be readily quantifiable. |
| Ancillary Environmental Impacts | Environmental impacts other than GHG emissions reductions, including public health and ecosystem impacts from changes in air quality or other environmental indicators. These impacts may not be readily quantifiable. |
| Ancillary Economic Impacts | Economic impacts other than direct costs or benefits of GHG reduction actions (e.g. economic development, cost savings for other actions). These impacts may not be readily quantifiable. |
| Equity Effects | Measure disproportionately affects a population, sector or a region of the state or affects the state’s competitive position relative to other states. These impacts may not be readily quantifiable. |
| Public and Political Support/Concern | Expected support and or concern from the general public and from policymakers. These impacts may not be readily quantifiable. |
| Feasibility | Ease of implementation and administration by implementing parties. These impacts may not be readily quantifiable. |
| Compatibility | Measure reinforces or enhances the effectiveness of other policy programs, or is required for other measures to work. These impacts may not be readily quantifiable. |
| Transferability to Other States/Nationally | Ease of duplication of measure in other states and or national and international policies. These impacts may not be readily quantifiable. |

- Potential Energy Supply & Solid Waste GHG Reduction Opportunities –Edited 12-17-03

The following notation was used in the table below:

- *Options that were popular choices in other states, potentially high Maine GHG reduction options, or both (originally denoted by CCAP, reviewed by Stakeholders

- *?  For *’d options to which at least one member of the Stakeholder Advisory Group expressed uncertainty about it being important in Maine

- *! For options not previously marked with a *, which at least one member of the Stakeholder Advisory Group thought should be a priority

- Some additional comments from stakeholders are highlighted in the list

| Energy Supply Sector GHG Reduction Opportunities |
| --- |
| 1 | Renewable Energy Policies |
| 1.1 | *Renewable Portfolio Standards (RPS) - Renewable portfolio standards mandate a certain minimum percentage of annual electricity production or sales come from renewable energy sources. Sources of qualifying renewable energy are delineated in the legislation, as are increased percentage requirements over time. RPS policies typically include wind and solar, and may include biomass, hydrogen (produced with renewable energy), tidal and small hydroelectric generation. |
| 1.1.a | Green tags within regional power pool – Green tags are certificates representing the air quality benefits of renewable power. These certificates may be sold separately from the power generated by the renewable energy source, enabling more flexible and cost-effective compliance with renewable portfolio standards. |
| 1.2 | *Renewable Energy Public Benefit Fund (PBF)/System Benefit Charge (SBC) - States generally collect funding as a charge on electricity rates or as a lump-sum payment from utilities, and then redistribute the money to projects such as wind farms, fuel cell deployment programs, and solar energy systems. |
| 1.3 | Wind Turbine on Farm – Renewable providers pay farmers for rights to place wind turbines on farmland that has appropriate wind resources. |
| 1.4 | Green Power Purchases |
| 1.4.a | *State Green Power Purchases – A requirement that State government and universities meet a minimum percent of their power needs with renewable energy. The renewable energy percentage may be set to increase over time. |
| 1.4.b | Local and University Green Power Purchases – see 1.5.a |
| 1.4.c | Green Power Marketing – Marketing and sales of green power in the competitive marketplace, in which multiple suppliers and service offerings exist. |
| 1.4.d | Green Pricing - Green pricing is an optional utility service that allows customers an opportunity to pay a premium (usually per kWh) on their electric bill to cover the extra cost of renewable energy generation and create demand for additional investment. |
| 2 | Advanced Low-emitting Technologies |
| 2.1 | Integrated Gasification Combined Cycle (IGCC) – Pressurizing coal to produce a mixture of carbon monoxide (CO) and hydrogen (H2), known as synthesis gas (syngas). Syngas is clean-burning (in terms of conventional pollutants). Additional processing with catalysts and separation can create a pure stream of H2 for combustion and CO2 for capture and sequestration. |
| 2.2 | *?Carbon Capture and Sequestration (CCS) – Several technologies allow carbon dioxide to be removed from flue gases for storage in geologic formations or in the ocean. May be more long term. Dragon Products can provide more information. Contact Ann Thayer. |
| 2.3 | FutureGen – The Federal Government’s IGCC+CCS+H2 production demonstration project. |
| 2.4 | Clean Coal Technologies – Various new technologies that burn coal more cleanly or efficiently, reducing emissions of conventional pollutants and, in some cases, CO2. |
| 2.5 | Fuel Cells Incentive Policy – Use pure hydrogen as energy, or strip hydrogen from fossil fuels. Create electricity without combustion. |
| 2.6 | *Biomass Gasification (also in Ag, Forestry, Waste) – Pressurizing agricultural biomass to produce a synthesis gas for combustion. |
| 2.7 | *Biomass Co-firing (also in Ag, Forestry, Waste) – Combustion of agricultural biomass and fossil fuels together. |
| 3 | Other Supply Efficiency Measures |
| 3.1 | *Repowering Old Plants – Converting old plants to natural gas combined cycle (NGCC) or coal integrated gasification combined cycle (IGCC) technology. Both technologies have the potential to provide efficiency improvements and lower emissions per kWH. |
| 3.2 | Efficiency Improvements in Existing Plants – Upgrades to equipment or replacement of parts. |
| 3.3 | Nuclear Plant Relicensing – After the first 40 years of operation, nuclear plants can apply for license renewal to operate for up to 20 more years. Nuclear plants that do not relicense result in loss of zero/low-emission baseload generation that must be replaced by other power sources. (No nuclear plants exist in Maine. This applies to nuclear plants in adjoining states in the same electricity pool as Maine – the New England Power Pool.) |
| 3.4 | Nuclear Plant Uprating – Increasing output from an existing plant, by modifications to turbines and the steam system. (No nuclear plants exist in Maine. This applies to nuclear plants in adjoining states in the same electricity pool as Maine – the New England Power Pool.) |
| 3.5 | *?Hydrogen – Hydrogen is a clean burning fuel that may be produced by IGCC and other power sources. The extent to which emissions are lower depend on how it is produced. Unclear what used for? |
| 4 | Distributed Generation (DG) |
| 4.1 | *Combined Heat and Power Incentive Policy (CHP) - Reduce barriers and implement program to increase clean CHP in the state. CHP is a high efficiency method of DG that utilizes both the steam and electricity produced by the electricity generating process, rather than just the electricity. Efficiency can be 2-3 times that of systems not utilizing the heat produced. |
| 4.2 | Landfill Gas Recovery (also in Ag, Forestry, Waste) – Capture the methane gas (a high global warming potential GHG that is a natural by-product of landfills) for flaring (burning to convert it to CO2, a low global warming potential GHG) or for combusting for energy generation. |
| 4.3 | Waste-to-Energy (also in Ag, Forestry, Waste) - Waste-to-energy facilities produce energy through the combustion of municipal solid waste in specially designed power plants equipped with pollution control equipment to clean emissions. |
| 5 | Caps, Standards and Goals |
| 5.1 | *Regional / State Cap and Trade - Set a mandatory cap on the amount of CO2 emitted by the electricity generation sector. Reductions in emissions below cap levels result in tradable credits. Entities polluting at levels higher than permitted by the cap are required to purchase these emission credits. |
| 5.2 | *Remove?Emission Standards – Standards that limit emissions on an output basis. A CO2 emission standard often limits the tons of CO2 per kWh produced. A generation performance standard, or GPS, is an emission standard covering several pollutants in one policy/regulation, and can include CO2. |
| 5.3 | Carbon Intensity Targets – A standard for emissions per unit output or per economic value of the output. |
| 5.4 | GHG Purchase Program |
| 5.5 | Voluntary CO2 Targets – A program in which companies set their own targets and baselines and start to meet these targets. Sometimes a cap or emissions standard. Companies can choose to participate in third party programs (established by government agencies or nongovernmental organizations). |
| 5.6 | CO2 Tax – A tax applied upstream to carbon content of fuels or downstream to CO2 emissions. |
| 6 | Grid and Utility Policies |
| 6.1 | *!Interconnection Rules – Standardized rules to enable clean, distributed generation to receive authorization to connect to the local grid. |
| 6.2 | *!Remove Transmission Barriers – Transmission pricing and technical issues are often barriers to renewable and other clean distributed generation (DG), as well as power from independent power producers (IPPs) |
| 6.3 | Remove Utility Rate Barriers |
| 6.4 | Transmission System Upgrading – Improvements to the efficiency and/or reliability of the transmission system or “grid”. |
| 6.4.a | Reduce Transmission Line Loss – An efficiency improvement to a transmission system. |
| 6.5 | Net Metering - Allows the electric meters of customers with generating facilities to turn backwards when the generators are producing energy in excess of the customers' demand, enabling customers to use their own generation to offset their consumption over a billing period. Most/all basic meters are capable of doing this. |
| 6.6 | *Load Management – Programs that create incentives for electricity customers to reduce electricity load from the utility grid in response to emergency and/or market-based price signals. |
| 6.7 | Time-of-use Rates – Utilities can charge higher prices during peak periods to encourage customers to shift usage to other cheaper cost periods of the day. Similar to telephone rates that vary by the period of day. Requires installation of an advanced meter that tracks consumption during each rate period. |
| 6.8 | Real-time Pricing - Allow utilities to charge more during the times of the day when demand is greatest – and less when demand is lower. Prices are different from hour to hour and day to day. This would give consumers an incentive to use less energy during times of peak use. Requires installation of real-time meters (a type of advanced meter). |
| 6.9 | Advanced Metering – In conjunction with communications systems, enables energy providers to offer their customers time-based rates with off-peak discounts, allowing consumers to save on their electricity bills by varying their demand in response to price signals. Can also help determine how much energy is required to run a specific piece of equipment. Real-time meters are a subcategory of advanced meters. |
| 7 | Cross-Cutting Electricity Sector Measures |
| 7.1 | *Public Benefit Funds (PBF)/System Benefit Charge (SBC) – Funds created by a surcharge on electricity, natural gas or oil sales that are used to fund demand side energy efficiency, renewable energy, load management and conservation programs. |
| 7.2 | Research, Development and Demonstration (RD&D) – Policies, programs and incentives that support new research and development of renewable energy, low-emitting energy or energy efficiency technologies. |
| 7.3 | Tax Incentives – Funds from a state’s general budget that go to renewable energy, low-emitting energy or energy efficiency technologies or production. Tax incentives are often credited on a per-kWh generated (or saved) basis. |
| 7.4 | *Offset Requirements – Requirement to offset a given percentage of CO2 emissions through projects that reduce emissions indirectly, such as afforestation/reforestation or new renewable energy projects. |
| 7.5 | *Registry – Voluntary GHG emissions registry that requires participating entities to separately report direct and indirect emissions or emission reductions. Registries may be used to provide public recognition, baseline protection, and support future emissions trading regimes. |
| 7.6 | Brownfield Re-development – Policies to encourage or require that new power generation facilities be built on land formerly used for industrial/commercial purposes, rather than on forest or farmland. |
| 7.7 | Environmental Disclosure – Requirements that power providers disclose emissions on utility bills or in other public reports/venues. |
| 7.8 | Full Cost Accounting – Ensure that environmental impacts of power production are reflected in the cost of power. |
| 7.9 | *Public Education – Any of a variety of methods, including public service announcements and education in schools, that make the public aware of the GHG emissions that come from fossil-fueled electricity generation and the things people can do to reduce GHG emissions. |

| Solid Waste Management Sector GHG Reduction Opportunities |
| --- |
| 8 | Landfill Gas and Solid Waste Management |
| 8.1 | Landfill Methane Strategy |
| 8.1.a | Flare Landfill Methane – Combusting it turns methane (a high global-warming-potential gas) into CO2 (a low global-warming-potential) gas. |
| 8.1.b | *!Convert Landfill Methane to Energy - Landfills naturally create methane gas (a GHG) as a by-product. Rather than being released into the air or burned off (flared), methane can be captured and utilized as a fuel to produce energy. |
| 8.2 | Waste Management Strategy – The production of less municipal solid waste and or the means by which waste is handled after it is created can reduce GHG emissions. |
| 8.2.a | *Resource Recovery Facility – Burning waste can reduce the amount of methane generated from waste and can create a source of energy that avoids emissions from other energy sources. |
| 8.2.b | *Recycling/Source Reduction – Create programs to reduce the amount of waste being put in landfills and/or waste-to-energy facilities, thereby reducing the amount of methane and CO2 generated. Also, can reduce source emissions by reducing the need for virgin materials. |
| 9 | Wastewater Activities |
| 9.1 | Energy Efficiency Improvements – Reducing the amount of energy needed for wastewater facilities. |
| 9.2 | Lower Waste Processing Needs - Reduce water consumption and waste production. |
| 9.3 | Methane and Biogas Energy Programs – Capture methane emissions from wastewater facilities for use as a fuel source. |
| 9.3.a | Install digesters and turbines – Use captured methane as an energy source for turbines. |
| 9.3.b | Install fuel cells – Use captured methane as a fuel source for fuel cells. |

4.  Preliminary GHG Savings & Cost Estimates for Priority Measures

| Electricity and Waste Sector |
| --- |
| Preliminary GHG Savings & Cost Estimates for Priority Measures from 12/17 Meeting |
| Please see accompanying EW Assumptions Document to review underlying data needs, sources, and assumptions |
|  |  | Estimated Savings in 2010 | Estimated Savings in 2020 | Cost Effectiveness |
|  | Measure (Sector) | Thousand MTCO2 (Electricity) | Thousand MTCO2 (FF) | Thousand MTCO2 (Total) | Thousand MTCO2 (Electricity) | Thousand MTCO2 (FF) | Thousand MTCO2 (Total) | $/MTCO2 |
| EW 1 | Electricity Generation |  |  |  |  |  |  |  |
| 1.1 | Renewable Portfolio Standards | 236 |  | 236 | 373 |  | 373 | $18.4 in 2010 $18.7 in 2020 |
| 1.2 | Renewable Energy Public Benefit Fund/ System Benefit Charge |  |  |  |  |  |  |  |
|  | Biomass | 337 |  | 337 | 373 |  | 373 | $36.9 in 2010 $37.4 in 2020 |
|  | Other Renewables | 472 |  | 472 | 522 |  | 522 | $18.4 in 2010 $18.7 in 2020 |
| 1.3 | State Green Power Purchases | 2 |  | 2 | 6 |  | 6 | $55.3 in 2010 $56.1 in 2020 |
| 1.4 | Carbon Capture and Sequestration |  |  |  |  |  |  | NE |
| 1.5 | Biomass Gasification and Co-Firing | 217 |  | 217 | 214 |  | 214 | NE |
| 1.6 | Repowering Old Plants | 1,364 |  | 1,364 | 1,364 |  | 1,364 | NE |
| 1.7 | Hydrogen |  |  |  |  |  |  | NE |
| 1.8 | Combined Heat and Power Incentive Policy | 365 |  | 365 | 355 |  | 355 | NE |
| 1.9 | Regional Cap and Trade | 397 |  | 397 | 351 |  | 351 | $18.6 through 2020 |
| 1.10 | Emission Standards | 16 |  | 16 | 16 |  | 16 | NE |
| 1.11 | Interconnection Rules and Transmission Barriers |  |  |  |  |  |  | NE |
| 1.12 | Offset Requirements | 240 |  | 240 | 480 |  | 480 | NA |
| 1.13 | Registry |  |  |  |  |  |  | NE |
| 1.14 | Public Education |  |  |  |  |  |  |  |
| EW 2 | Waste Management |  |  |  |  |  |  |  |
| 2.1 | Convert Landfill Methane to Energy |  |  |  |  |  |  | NE |
| 2.2 | Resource Recovery Facility |  |  |  |  |  |  | NE |
| 2.3 | Recycling/ Source Reduction |  |  |  |  |  |  | NE |
|  | Total Savings (Thousand MTCO2e) | 3,646 |  | 3,646 | 4,054 |  | 4,054 |  |

NE = Not estimated

5.  Energy Supply & Solid Waste Assumption

| Measure: | EW 1.1 Renewable Portfolio Standards (RPS) |
| --- | --- |

# Sector:			Electricity Generation

Policy Description:	Renewable portfolio standards mandate a certain minimum percentage of annual electricity production or sales come from renewable energy sources.  Sources of qualifying renewable energy are delineated in the legislation, as are increased percentage requirements over time.  RPS policies typically include wind and solar, and may include biomass, hydrogen (produced with renewable energy), tidal and small hydroelectric generation.

# BAU Policy/Program:	Renewable Resource Portfolio Requirement: At least 30% of total kWh sales from each competitive electricity provider in Maine must come from eligible renewable sources.  Latter may include municipal solid waste plants, and combined heat and power units regardless of fuel type.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Maine PUC Report and Recommendations on the Promotion of Renewable Resources dated December 31, 2003, recommends repealing current portfolio requirement.  It also recommends creating two separate portfolio standards, one to promote biomass and/or municipal solid waste, another for hydro and other renewables.

# Current level of biomass is greater than the recommended 10% level, so no emissions impact has been estimated for this category.  (Note, however, that based on current information it appears that many existing biomass generating facilities in Maine may require subsidies to continue operating into the future.  It may therefore be useful to conduct an analysis to estimate the CO2 reductions from an RPS designed to support the continued operation of such facilities.)

# Emissions impact for an RPS based on the second category (renewable resources other than biomass and waste) has been estimated below.  Analysis assumes that baseline generation for these resources is zero.  New RPS assumed to be set at levels comparable to those in existing programs in Massachusetts and Connecticut.

# Maine renewable premium of $15/MWh assumed to be split between 2/3 biomass ($10/MWh), 1/3 hydro and other sources ($5/MWh).  All new renewable generation assumed to be in-state.

# It may also be useful to model the RPS at levels comparable to those as proposed in Connecticut and Rhode Island.

| Hydro and Other Renewable RPS Assumptions and Associated Emission Impacts |
| --- |
|  | 2010 | 2020 | Source |
| Total Electricity Demand (MWh) | 12,430,000 | 13,937,000 | Maine Energy Policy Report |
| RPS Level | 7% | 10% | 2010: CT RPS, Class I 2020: See Note |
| RPS Generation (MWh) | 870,100 | 1,393,700 | Calculated |
| Average Regional CO2 Emissions Rate (lb CO2/MWh) | 598 | 590 | IPM |
| Reduction in CO2 Emissions (Thousand MTCO2e) | 236 | 373 | Calculated |
| Renewable Energy Premium ($/MWh) | $15 | $15 | Maine Renewable Energy retail offer |
| Total Cost (million $) | $4.35 | 6.97 |  |
| Cost per metric ton | $18.4 | $18.7 | Calculated |

*2020 RPS level based on assumption that Maine level would be approximate to but

lower than associated level in Massachusetts (15%).

| Measure: | EW 1.2 Renewable Energy Public Benefit Fund (PBF)/ |
| --- | --- |
|  | System Benefit Charge (SBC) |

# Sector:	Electricity Generation

Policy Description:	States generally collect funding as a charge on electricity rates or as a lump-sum payment from utilities, and then redistribute the money to projects such as wind farms, fuel cell deployment programs, and solar energy systems.

BAU Policy/Program:	No mandatory system.  Existing Renewable Resource Research and Development Fund allows electricity customers to make voluntary contributions through their utility bills to a fund which supports 1) renewable resource R&D at universities, and 2) demonstration projects using renewable energy technologies by Maine-based non-profit organizations, consumer-owned electric cooperatives and community action programs.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

For preliminary analysis, following assumptions were made:

# System charges assumed to be used to fund production tax credits for new biomass units (at $0.0010 / kWh) and new small hydro and other units (at $0.0007 / kWh).  These charge levels were taken from the recommendations in the Maine PUC Renewable Resources report.

# Production tax credits are set equal to the renewable premium.

# Biomass assumed to be carbon-neutral

# Maine renewable premium of $15/MWh assumed to be split between 2/3 biomass, 1/3 hydro and other sources.  All new renewable generation assumed to be in-state.

| Data Need | 2010 | 2020 | Source |
| --- | --- | --- | --- |
| Charge* | $0.0010 / kWh for biomass $0.0007 / kWh for other renewables | $0.0010 / kWh for biomass $0.0007 / kWh for other renewables | Maine PUC Renewable Report recommendation |
| Total electricity sales (MWh) | 12,430,000 | 13,937,000 | Maine Energy Policy Report |
| Total funding available | $ 12.4 million for biomass $ 8.7 million for other renewables | $ 13.9 million for biomass $ 9.8 million for other renewables | Calculated |
| Renewable premium | $10 / MWh for biomass $5 / MWh for other renewables | $10 / MWh for biomass $5 / MWh for other renewables | Based on Maine Renewable Energy retail offer |
| Total new renewable generation (MWh) | 1,243,000 for biomass 1,740,200 for other renewables | 1,393,700 for biomass 1,951,180 for other renewables | Calculated |
| Average Regional CO2 Emissions Rate (lb CO2/MWh) | 598 | 590 | IPM |
| Reduction in CO2 Emissions (Thousand MTCO2e) | 337 for biomass 472 for other renewables | 373 for biomass 522 for other renewables | Calculated |
| Cost per metric ton | $36.9 for biomass $18.4 for other renewables | $37.4 for biomass $18.7 for other renewables | Calculated |

*Suggested charge levels are similar to current levels in other New England states including

Massachusetts ($0.0005 / kWh) and Connecticut ($0.0010 / kWh).

| Measure: | EW 1.3 State Green Power Purchases |
| --- | --- |

# Sector:	Electricity Generation

Policy Description:	A requirement that State government and universities meet a minimum percent of their power needs with renewable energy.  The renewable energy percentage may be set to increase over time.

BAU Policy/Program:	Governor of Maine has set a goal for the State government to purchase 50% of its electricity from renewable sources.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

For preliminary analysis, following assumptions were made:

# Increase in state government purchase level to 60% in 2010 and 75% in 2020, all from 100% renewable sources

# Current 50% government purchase level taken as baseline.  (Note, however, that if the state purchase policy was developed after the relevant legislation was passed, it may be appropriate to model the current 50% purchase level as the new policy level instead of as the BAU baseline.  In this case, the emission reductions from the policy presented below may increase.)

# State average renewable generation level remains constant through 2020

# All renewable generation assumed to be in-state.

| State Green Power Assumptions and Associated Emission Impacts |
| --- |
| Data Need | 2010 | 2020 | Source |
| Total State Electricity Demand (MWh) | 138,604 | 154,180 | Estimated based on Maine Energy Policy Report |
| Maine Renewable Generation Level | 40% | 40% | State data |
| State Government Purchase Baseline | 50% | 50% | BAU policy |
| State Government Purchase Level | 60% | 75% | Assumption |
| BAU State Renewable Share (MWh) | 97,023 | 107,926 | Calculated |
| New State Renewable Share (MWh) | 105,339 | 131,053 | Calculated |
| Average Regional CO2 Emissions Rate (lb CO2/MWh) | 598 | 590 | IPM |
| Reduction in CO2 Emissions (Thousand MTCO2e) | 2.3 | 6.2 | Calculated |
| Renewable Energy Premium ($/MWh) | $15 | $15 | Maine Renewable Energy retail offer |
| Total Cost (million $) | 0.125 | 0.347 | Calculated |
| Cost per metric ton | 55.3 | 56.1 | Calculated |

| Measure: | EW 1.4 EW 1.4 Carbon Capture and Sequestration (CCS) |
| --- | --- |

# Sector:	Electricity Generation

Policy Description:	Several technologies allow carbon dioxide to be removed from flue gases for storage in geologic formations or in the ocean.  May be a more long-term measure.

BAU Policy/Program:

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Inventory of generating units in Maine | TBD | EGRID |
| List of suitable locations for storage | TBD | TBD |
| Total CO2 storage capacity (thousand tons) | TBD | TBD |
| Performance data of storage/capture technology | TBD | TBD |
| Total annual emissions from generating plants (Thousand MTCO2e) | TBD | Calculated |
| Reduction in CO2 Emissions (Thousand MTCO2e) | TBD | Calculated |

| Measure: | EW 1.5 EW 1.5 Biomass Gasification and Co-firing |
| --- | --- |

# Sector:	Electricity Generation

Policy Description:	Pressurizing agricultural biomass to produce a synthesis gas for combustion.  Agricultural biomass may also be combusted together with fossil fuels.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

For preliminary analysis, following assumptions were made:

# Biomass is assumed to be carbon neutral

| Data Need | 2010 | 2020 | Source |
| --- | --- | --- | --- |
| Potential quantity of biomass available in Maine as fuel | TBD | TBD | TBD |
| Total potential electric generation using biomass (MWh) | 3,200,000 | 3,200,000 | DOE (data and methodology used to estimate this value was not provided)* |
| Assumed proportion of total potential that can be utilized | 25% | 25% | Assumption |
| Average Regional CO2 Emissions Rate (lb CO2/MWh) | 598 | 590 | IPM |
| Reduction in CO2 Emissions (Thousand MTCO2e) | 217 | 214 | Calculated |

# *Biomass generation potential available at http://www.eere.energy.gov/state_energy/tech_biomass.cfm?state=ME

| Measure: | EW 1.6 Repowering Old Plants |
| --- | --- |

# Sector:	Electricity Generation

Policy Description:	Converting old plants to natural gas combined cycle (NGCC) or coal integrated gasification combined cycle (IGCC) technology.  Both technologies have the potential to provide efficiency improvements and lower emissions per kWh.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

For preliminary analysis, following assumptions were made:

# Total annual electric load in aggregate served by original plants assumed to be served by new plants.

# All oil-fired plants above 100 MW replaced by NGCC units with efficiency of 50%.  All coal-fired plants above 100 MW replaced by IGCC units with efficiency of 40%.

# Total annual capacity, fuel input and generation for existing plants taken from EGRID year 2000 data.

# Note that two plants (one coal- and one oil-fired) repowered were CHP plants.

# Total reductions are very high because the plants repowered had low efficiencies and accounted for a large share (almost 60%) of CO2 emissions from the Maine electric power industry in 2000.  One large plant alone accounted for 37% of emissions in 2000.

| Data Need | Assumption | Source |
| --- | --- | --- |
| Number of coal- and oil-fired plants |  | EGRID |
| Coal | 1 |  |
| Oil | 3 |  |
| Total | 4 |  |
| Total capacity repowered (MW) |  | EGRID |
| Coal | 102 |  |
| Oil | 1,222 |  |
| Total | 1,324 |  |
| Total annual emissions baseline (Thousand MTCO2e) |  | Calculated |
| Coal | 704 |  |
| Oil | 2,070 |  |
| Total | 2,774 |  |
| Total annual emissions after repowering (Thousand MTCO2e) |  | Calculated |
| Coal | 518 |  |
| Oil | 892 |  |
| Total | 1,410 |  |
| Reduction in CO2 Emissions (Thousand MTCO2e) |  | Calculated |
| Coal | 186 |  |
| Oil | 1,178 |  |
| Total | 1,364 |  |

# Note: Reductions assumed to be the same in 2010 and 2020

| Measure: | EW 1.7 Hydrogen |
| --- | --- |

# Sector:	Electricity Generation

Policy Description:	Hydrogen is a clean burning fuel that may be produced by IGCC and other power sources and can be used to generate electricity.  The magnitude of the resulting emission reductions depends on how the hydrogen is produced.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Requires detailed information on hydrogen production method, cost and performance data of hydrogen units.

| Measure: | EW 1.8 Combined Combined Heat and Power (CHP) Incentive Policy |
| --- | --- |

# Sector:	Electricity Generation

Policy Description:	Reduce barriers and implement programs to increase clean CHP in the state.  CHP is a high efficiency method of DG that utilizes both the steam and electricity produced by the electricity generating process, rather than just the electricity.  Efficiency can be 2-3 times that of systems not utilizing the heat produced.

BAU Policy/Program:	CHP units are included as eligible renewable sources under the state Renewable Resource Portfolio Requirement (for a description of this state program see Renewable Portfolio Standards [RPS] measure above).

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

For preliminary analysis, following assumptions were made:

# EEA MW potential represents technical potential only, and does not evaluate economic potential.  EEA assumes commercial units are reciprocating engines less than 5 MW, industrial units are simple-cycle combustion turbines of 5-10 MW capacity.

# Based on EGRID data, CHP capacity factor assumed to be 0.4 for commercial, 0.6 for industrial.

# CHP electric efficiency assumed to be 0.4 for both.

# Power-to-heat ratio assumed to be 0.8 for all units based on units of similar capacity in EGRID.

# All CHP units assumed to be fired by natural gas.

# Fuel input of stand-alone boilers replaced assumed to be 2/3 gas, 1/3 oil (Btu basis).  Oil is assumed to be distillate fuel.

# Efficiency of stand-alone boilers assumed to be 80%.

| Data Need | 2010 | 2020 | Source |
| --- | --- | --- | --- |
| Total Maine potential CHP capacity (MW) |  |  | EEA |
| Commercial | 411 | 411 |  |
| Industrial | 232 | 232 |  |
| Total | 643 | 643 |  |
| Total annual CHP emissions (Thousand MTCO2e) |  |  | Calculated |
| Commercial | 652 | 652 |  |
| Industrial | 552 | 552 |  |
| Total | 1205 | 1,205 |  |
| Total annual boiler emissions displaced (Thousand MTCO2e) |  |  | Calculated |
| Commercial | 459 | 459 |  |
| Industrial | 389 | 389 |  |
| Total | 848 | 848 |  |
| Average Regional CO2 Emissions Rate (lb CO2/MWh) | 598 | 590 | IPM |
| Total annual grid emissions displaced (Thousand MTCO2e) |  |  | Calculated |
| Commercial | 391 | 385 |  |
| Industrial | 331 | 326 |  |
| Total | 721 | 712 |  |
| Maximum Reduction in CO2 Emissions (Thousand MTCO2e) |  |  | Calculated |
| Commercial | 197 | 192 |  |
| Industrial | 167 | 163 |  |
| Total | 365 | 355 |  |

Note: Totals may not sum due to rounding

| Measure: | EW 1.9 Regional Cap and Trade |
| --- | --- |

Sector:			Electricity Generation

Policy Description:	Set a mandatory cap on the amount of CO2 emitted by the electricity generation sector.  Reductions in emissions below cap levels result in tradable credits.  Entities polluting at levels higher than permitted by the cap are required to purchase these emission credits.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

For preliminary analysis, following assumptions were made:

# ICF Consulting’s Integrated Planning Model (IPM) was used to estimate the CO2 emission reductions and cost savings from the implementation of a 10-state regional CO2 cap and trade program.  The states included were Connecticut, Delaware, Maine, Massachusetts, New Hampshire, New Jersey, New York, Pennsylvania, Rhode Island, and Vermont.

# Regional CO2 emission cap set at 1990 levels in 2010, 10% below 1990 levels in 2020

# Assumes no offsets allowed in 2010, forestry and high GWP gas offsets up to 10% of total cap allowed in 2020

# Note that this analysis models only a regional emission cap.  Different emission reduction and cost levels will likely be obtained if state-specific energy policies (e.g., an RPS) are put into place in Maine along with the regional cap.

| Impact | 2010 | 2020 | Source |
| --- | --- | --- | --- |
| Maine Proportion of NEPOOL CO2 Emissions | 11.4% | 10.2% | Estimated using EPA Base Case 2003 IPM data |
| Total 10-state CO2 Reduction (Thousand MTCO2e) | 33,796 | 68,210 | IPM cap and trade run |
| Total NEPOOL CO2 Reduction (Thousand MTCO2e) | 3,479 | 3,436 | IPM cap and trade run |
| Reduction in Maine CO2 Emissions (Thousand MTCO2e) | 397 | 351 | Calculated |
| Total 10-state Program Cost (NPV through 2020, Million Year 2000$) | NA | $8,198 | IPM |
| Total Maine Program Cost (NPV through 2020, Million Year 2000$) | NA | $836 | Calculated |
| Cost per metric ton | NA | $18.60 | Calculated |

| Measure: | EW 1.10 Emission Standards |
| --- | --- |

Sector:			Electricity Generation

# Policy Description:	Standards that limit emissions on an output basis.  A CO2 emission standard often limits the tons of CO2 per kWh produced.  A generation performance standard, or GPS, is an emission standard covering several pollutants in one policy/regulation, and can include CO2.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

For preliminary analysis, following assumptions were made:

# Emission standard adopted for CO2 only, applied to all fossil-fired plants in Maine.

# Emission rates of plants in IPM adjusted to meet standard.  No plants shut down, all plants assumed to comply with plant improvements, fuel switching or offset purchases.

# Note that an emission standard may be used in conjunction with a requirement to offset the CO2 emissions through investment in afforestation/reforestation or new renewable energy projects.  Emission standards may allow generators to meet all or part of the emission limit through purchases of offsets; the carbon sequestered or reduced is then deducted from the actual CO2 emissions from the plant to help meet the standard.

| Impact | 2010 | Source |
| --- | --- | --- |
| Emission Limit (lb CO2/MWh) | 1,100 | Massachusetts Regulation 310 CMR 7.29 |
| Reduction in CO2 Emissions (Thousand MTCO2e) | 371 | Estimated using EPA Base Case 2000 IPM data |
| Emission Limit (lb CO2/MWh) | 1,800 | NESCAUM Final Model Rule |
| Reduction in CO2 Emissions (Thousand MTCO2e) | 15.8 | Estimated using EPA Base Case 2000 IPM data |

Note: Reductions in 2020 would be approximately the same as those in 2010

| Measure: | EW 1.11 Interconnection Rules and Transmission Barriers |
| --- | --- |

Sector:	Electricity Generation

Policy Description:  	Standardized rules to enable clean, distributed generation to receive authorization to connect to the local grid.  Transmission pricing and technical issues are often barriers to renewable and other clean distributed generation (DG), as well as power from independent power producers (IPPs).

# BAU Policy/Program:

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Will require specific rule(s) proposed and associated estimate of potential capacity increase

| Measure: | EW EW 1.12 Offset Requirements |
| --- | --- |

# Sector:	Electricity Generation

Policy Description:	Requirement to offset a given percentage of CO2 emissions through projects that reduce emissions indirectly, such as afforestation/reforestation or new renewable energy projects.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

Offset Requirements may be used in conjunction with a GHG cap and trade program or an emission standard.  The GHG savings estimated in conjunction with the Emission Standards option (see above) could also result from a requirement to offset an equivalent quantity of emissions at plants that exceed the standard.

For preliminary analysis, following assumptions were made:

# All fossil-fired generating plants in Maine greater than 50 MW offset 5% of total annual emissions in 2010 and 10% in 2020.

| Impact | 2010 | 2020 | Source |
| --- | --- | --- | --- |
| Total Fossil-Fired CO2 Emissions (Thousand MTCO2e) | 4.94 | 4.96 | EPA Base Case 2003 IPM data |
| Offset Requirement | 5% | 10% | Assumption |
| Total CO2 Emissions Offset (Thousand MTCO2e) | 240 | 480 | Calculated |
| Offset Cost per MTCO2e | $10 | $17 | Assumption based on IPM results of cap and trade policies |
| Total Cost (Million $) | $2.40 | $8.16 | Calculated |

| Measure: | EW 1.13 Registry |
| --- | --- |

# Sector:	Electricity Generation

# Policy Description:	Voluntary GHG emissions registry that requires participating entities to separately report direct and indirect emissions or emission reductions. Registries may be used to provide public recognition, baseline protection, and support future emissions trading regimes.

BAU Policy/Program:	None

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Measure: | EW 1.14 Public Education |
| --- | --- |

# Sector:	Electricity Generation

Policy Description:	Any of a variety of methods, including public service announcements and education in schools, that make the public aware of the GHG emissions that come from fossil-fueled electricity generation and the actions people can take to reduce GHG emissions.

# BAU Policy/Program:

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Measure: | EW 2.1 EW 2.1 Convert Landfill Methane to Energy |
| --- | --- |

Sector:			Waste Management

Policy Description:	Landfills naturally create methane gas (a GHG) as a by-product.  Rather than being released into the air or burned off (flared), methane can be captured and utilized as a fuel to produce energy.

BAU Policy/Program:   	Gas-to-energy projects are in operation, under construction or planned at eleven Maine landfills (US EPA Landfill Methane Outreach Program).

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Inventory of Maine landfills | TBD | US EPA |
| Total potential landfill methane available (cubic feet) | TBD | US EPA |
| Typical operating parameters for existing landfill methane units | TBD | TBD |
| Total annual generating unit emissions (Thousand MTCO2e) | TBD | Calculated |
| Total annual methane consumed as fuel (Thousand MTCO2e) | TBD | Calculated |
| Total annual grid emissions displaced (Thousand MTCO2e) | TBD | Calculated |
| Reduction in CO2 Emissions (Thousand MTCO2e) | TBD | Calculated |

| Measure: | EW 2.2 Resource Recovery Facility |
| --- | --- |

# Sector:	Waste Management

Policy Description:	Burning waste can reduce the amount of methane generated from waste and can create a source of energy that avoids emissions from other energy sources.

BAU Policy/Program:   	Electric generating plants fired by municipal solid waste are included as eligible renewable sources under the state Renewable Resource Portfolio Requirement (for a description of this state program see Renewable Portfolio Standards [RPS] measure above).

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

| Data Need | Assumption | Source |
| --- | --- | --- |
| Total waste discarded annually (tons) | TBD | TBD |
| Methane emissions from solid waste available (cubic feet) | TBD | TBD |
| Typical operating parameters for existing Maine waste-to-energy units | TBD | TBD |
| Total annual generating unit emissions (Thousand MTCO2e) | TBD | Calculated |
| Total annual methane consumed as fuel (Thousand MTCO2e) | TBD | Calculated |
| Total annual grid emissions displaced (Thousand MTCO2e) | TBD | Calculated |
| Reduction in CO2 Emissions (Thousand MTCO2e) | TBD | Calculated |

| Measure: | EW 2.3 EW 2.3 Recycling/Source Reduction |
| --- | --- |

# Sector:	Waste Management

Policy Description:	Create programs to reduce the amount of waste being put in landfills and/or waste-to-energy facilities, thereby reducing the amount of methane and CO2 generated.  Also, can reduce source emissions by reducing the need for virgin materials.

BAU Policy/Program:   	The Maine Legislature has established a goal of recycling 50% of the state's municipal solid waste by 2003.  A 37.3% statewide recycling rate was achieved by Maine residents and businesses in 2001.

# Data Needs, Sources & Assumptions for Preliminary GHG Savings and Cost Estimates:

# Will need to select specific recycling programs to be modeled (e.g., pay-as-you-throw, commercial resource management) and levels

# Will require information on current recycling baseline